## Slide 1
ATMOS
Scaling AI inference beyond accelerator memory
High-bandwidth flash + efficient acceleration for capacity-led enterprise and edge workloads
MORE MODEL CAPACITY
LESS SCALE-OUT FRICTION
MEASURABLE POC
01

## Slide 2
Enterprise AI Workload constraint
More than compute, Enterprise AI Platform are constrained by
Model growth, long context, concurrency and deployment limits compound into cost and engineering pressure.
01
Model and context do not fit
Large models, MoE experts and KV cache compete for limited accelerator memory.
02
Scaling adds software complexity
Tensor, pipeline and expert parallelism increase tuning, testing and failure domains.
03
Data movement taxes the system
Per-token communication can consume fabric bandwidth and create tail-latency risk.
04
Power and footprint cap deployment
Rack density, cooling, edge envelopes and utilization shape what is economically viable.
[Confidential]
©2026 SANDISK CORPORATION OR ITS AFFILIATES
Illustrative — validate against customer workload and approved product configuration.
02

## Slide 3
How ATMOS solves the Enterprise AI serving constraints
A media tier between working memory and conventional storage
HBF is intended to bring flash-scale capacity and high bandwidth closer to the accelerator data path.
Memory hierarchy
SRAM
Active compute state
LPDDR / HBM
Hot weights + active KV
HBF
Model weights + reusable KV
Host / NVMe
Repository + cold assets
ATMOS CARD CONCEPT
HBF MEDIA
MEMORY FABRIC
NPU
LPDDR
[Confidential]
©2026 SANDISK CORPORATION OR ITS AFFILIATES
Illustrative — validate against customer workload and approved product configuration.
03
Up to 1 TB
HBF capacity direction
Up to 128 GB
LPDDR working-memory direction
Up to 512 TOPS
INT8 / FP8 compute direction
<200 W class
Performance-profile direction

## Slide 4
WHAT WE ARE BUILDING
Eight compute-and-memory modules form one ATMOS card
A high-capacity model tier beside local NPU execution and working memory.
CONFIDENTIAL | ©2026 SANDISK
SOURCE DESIGN TARGETS
03
Sources: I3, I1 · Details in notes
ATMOS PCIE ADD-IN CARD
MODULE 1
HBF
NPU + LPDDR
MODULE 2
HBF
NPU + LPDDR
MODULE 3
HBF
NPU + LPDDR
MODULE 4
HBF
NPU + LPDDR
MODULE 5
HBF
NPU + LPDDR
MODULE 6
HBF
NPU + LPDDR
MODULE 7
HBF
NPU + LPDDR
MODULE 8
HBF
NPU + LPDDR
~1 TB
HBF model-capacity direction
128 GB
LPDDR working-memory direction
200 W class
Card power budget—not measured draw
Aggregated capacity is not uniform shared memory. Keep the model layout aware of each module.
Notes: SLIDE 3: Eight compute-and-memory modules form one ATMOS card EVIDENCE: SOURCE DESIGN TARGETS TALK TRACK The supplied card concept contains eight local NPU/HBF/LPDDR modules. Larger model capacity can stay on the card, while local working memory handles active state. This is the physical basis for the proposed finer-grained serving model. DETAILS AND LIMITS The IMA diagram lists up to 128 GB HBF and 8–16 GB LPDDR per module, plus local SRAM/NoC. V5 normalizes the card HBF direction to 1,000 decimal GB when calculating reserve budgets, rather than mixing GB and GiB. Card-level working memory uses the upper 128 GB option only where labeled. The 200 W class comes from the supplied product direction, not measured consumption. Mixed TOPS/TFLOPS source labels are not used to predict throughput. SOURCES — reviewed September 13, 2026 I3: IMA Card, user-supplied September 12 screenshot, marked 00.014 User-supplied internal material Eight NPU/HBF/LPDDR modules; 128 GB and 200 GB/s HBF/module, 8–16 GB and 50 GB/s LPDDR/module; Gen6 x4 module and Gen5 x16 card connections. Revision-dependent. I1: SNDK-ATMOS-Customer-v3(1).pptx User-supplied internal material Narrative, warm theme, chart families; illustrative winning regions are not validated results.

## Slide 5
LATENCY BUDGETS
Make the customer’s time budget visible
Practical request shapes in seconds—planning inputs, not platform benchmarks or p99 measurements.
CONFIDENTIAL | ©2026 SANDISK
ILLUSTRATIVE SERVICE BUDGETS
16
Sources: I7 · Details in notes
Chart: Seconds
| 4K / 256 out | 8K / 512 out | 32K / 1,024 out
Prefill | 2 | 6 | 20
Decode | 12 | 28 | 80
Exposed tier / launch | 2 | 6 | 20
Where ATMOS aims to help
Keep model state near compute.
Reduce avoidable activation waits.
Avoid capacity-driven coordination.
Queues, retrieval and tools add more time outside these bars.
The short-, medium- and long-call means (16 / 40 / 120 s) also drive the active-concurrency sizing.
Notes: SLIDE 16: Make the customer’s time budget visible EVIDENCE: ILLUSTRATIVE SERVICE BUDGETS TALK TRACK Rather than arbitrary unit-less platform latency bars, the service has explicit request shapes and time budgets. These inputs let us calculate concurrency and discuss which spans hardware or scheduling could improve. They are not a prediction of either platform. DETAILS AND LIMITS D7 totals 16/40/120 seconds from prefill, decode and exposed-tier/launch components. These are the same assumed mean active times as D2. Decode targets imply different output rates, but no hardware profile has established them. API queue, retrieval, OCR, external tool waits and result writing are separate spans. For a 120-second LLM step plus 10 seconds of serial tools, the combined time is 130 seconds before other stages. Do not sum per-stage p99s into an end-to-end p99 or label these means as SLO results. CALCULATION FILES D7_time_budgets SOURCES — reviewed September 13, 2026 I7: ATMOS Financial Services AI Workload and GTM Reference v2 User-supplied internal material Multi-model private inference, reviewed sector workflows, smallest suitable model, hybrid routing.

## Slide 6
LARGE MOE PLACEMENT
Compare a complete serving group—not just card capacity
Illustrative 235B-class FP8 model pack: 250 GB, including a provisional layout allowance.
CONFIDENTIAL | ©2026 SANDISK
CAPACITY-LED PLACEMENT EXAMPLE
13
Sources: I3, R1, R9, R11 · Details in notes
RTX RESIDENT GROUP
4 GPU cards
GPU 1
GPU 2
GPU 3
GPU 4
250 GB weights in 384 GB GDDR
~96 GB logical KV after a 10% reserve
Two dual-GPU 2U nodes—or a larger GPU host
ATMOS GROUP TO QUALIFY
1 card / 8 modules
1
2
3
4
5
6
7
8
250 GB weights in the HBF target
96 GB KV from a 128 GB LPDDR option
Internal TP / EP / pipeline coordination remains
This is a residency comparison—not a 4× throughput or replacement claim. Smaller GPU packs/offload remain alternatives.
Notes: SLIDE 13: Compare a complete serving group—not just card capacity EVIDENCE: CAPACITY-LED PLACEMENT EXAMPLE TALK TRACK ATMOS may reduce capacity-driven inter-card sharding for a large model. But a complete card still coordinates eight modules. The fair result is the accepted throughput and operating cost of a complete serving group, not a simple ratio of HBF and GDDR capacities. DETAILS AND LIMITS D5 assumes a 250 GB compiled pack for a 235B-class FP8 model, not a verified checkpoint size: about 235 GB raw plus a provisional layout allowance. Four RTX cards provide 384 GB; reserving 38.4 GB leaves 95.6 GB KV after weights. ATMOS stores the pack within a 900 GB HBF budget and separately budgets 96 GB KV in 128 GB LPDDR. Logical KV fits roughly 15 full 32K sequences in either example before extra duplication. Valid per-rank placement, shared parameters and operator support must be checked. A compact dual-GPU server makes RTX TP4 cross two nodes, but a 4U/8-GPU OEM system can keep it within one host; include that alternative rather than forcing a poor control. CALCULATION FILES D5_moe_memory SOURCES — reviewed September 13, 2026 I3: IMA Card, user-supplied September 12 screenshot, marked 00.014 User-supplied internal material Eight NPU/HBF/LPDDR modules; 128 GB and 200 GB/s HBF/module, 8–16 GB and 50 GB/s LPDDR/module; Gen6 x4 module and Gen5 x16 card connections. Revision-dependent. R1: NVIDIA RTX PRO 6000 Blackwell Server Edition https://www.nvidia.com/en-us/data-center/rtx-pro-6000-blackwell-server-edition/ 96 GB GDDR7; 1,597 GB/s; PCIe; public specifications, not workload measurements. R9: Qwen3-235B-A22B config https://huggingface.co/Qwen/Qwen3-235B-A22B/raw/main/config.json 94 layers, 4 KV heads, head dimension 128; 128 experts and top-8; all proposed baseline contexts <=32K including output. R11: vLLM expert-parallel deployment https://docs.vllm.ai/en/latest/serving/expert_parallel_deployment/ Expert execution and attention/expert group distinctions; current API support does not imply ATMOS support.

## Slide 7
PERFORMANCE SENSITIVITY
Residency helps when avoided waiting exceeds its own cost
A conditional time model—not a silicon forecast or an automatic HBF winner map.
CONFIDENTIAL | ©2026 SANDISK
ANALYTICAL BREAK-EVEN
15
Sources: I2, I4, I6 · Details in notes
Exposed tier waiting in the reference service
0%
10%
20%
30%
40%
50%
Other work
0% slower
105
98
90
83
75
68
Other work
10% slower
115
107
98
90
81
73
Other work
25% slower
130
120
110
100
90
80
Other work
50% slower
155
143
130
117
105
93
Reference = 100
Lower is better.
Assume 4× less exposed tier wait and 5% extra software overhead.
At +25% other-work time, break-even is ~30% initial waiting.
Replace both the execution and transfer assumptions with measured profiles. Capacity alone cannot establish a speedup.
Notes: SLIDE 15: Residency helps when avoided waiting exceeds its own cost EVIDENCE: ANALYTICAL BREAK-EVEN TALK TRACK This retains the useful V3 break-even visual but the cells are calculable time indices, not unsupported platform winners. It shows both favorable and unfavorable outcomes. DETAILS AND LIMITS D6: candidate/reference service time = (1–f)c + f/4 + 0.05. f is exposed addressable waiting, not the fraction of cold experts or the cache miss rate. c is the multiplier of remaining work. Assumptions 4× and 5% are explicitly chosen sensitivity inputs, not derived from peak HBF/GDS ratios. With c=1.25 the crossover is f=0.30. A lower-latency transfer only matters when it eliminates critical-path waiting; queues and full-service performance are separate. CALCULATION FILES D6_break_even SOURCES — reviewed September 13, 2026 I2: SNDK-ATMOS-Customer-v4(1).pptx User-supplied internal material Evidence discipline, module/card topology, OEM/NUMA, analytical models. I4: ATMOS_HBF_OEM_Platform_and_LLM_Evaluation_Plan_v3.md User-supplied internal material Topology, realistic OEM qualification, runtime and LLM/RAG separation. I6: 01-tokensim-hbf-emulator.md User-supplied internal material Limited KV-far-tier abstraction; MoE event extension and calibration are required.

## Slide 8
Choice Heatmap: Context Length vs Concurrency
Illustrative winner map for high-reuse, large-document MoE/RAG workload. Replace with measured POC output.
v3 workload-fit
Colors show likely best-fit region, not guaranteed performance.
RTX/GPU
RTX+CXL
ATMOS/HBF
No-fit/measure
8K
16K
32K
64K
128K
Context length
Concurrent jobs
256
RTX + CXL
ATMOS
ATMOS
ATMOS
NO-FIT?
128
RTX
ATMOS
ATMOS
ATMOS
64
RTX
RTX + CXL
RTX + CXL
ATMOS
ATMOS
32
RTX
RTX
RTX + CXL
ATMOS
ATMOS
8
RTX
RTX
RTX
RTX + CXL
ATMOS
How to read this
Low context and low concurrency often favor RTX because everything fits in fast memory. As context, concurrency, and reusable MoE/KV working set grow, warm capacity and persistent HBF become more interesting. Extreme cells require measurement because queueing, tools, and tail latency can dominate.
Assumption: high reuse/locality. With low reuse or random small transfers, shift cells left toward RTX/no-fit.
RTX + CXL
ATMOS

## Slide 9
Parameter Levers That Shift the Winner
The platform choice moves when workload shape changes. These are the knobs to sweep in the POC.
v3 workload-fit
Direction is illustrative; final winner comes from SLO-qualified accepted-task results.
Pushes RTX/GPU
Pushes RTX+CXL
Pushes ATMOS/HBF
Blocks all / no-fit
Small active model
short context
low switching
strict interactive SLO
Warm overflow
moderate reuse
real CXL device
stable staging path
Large MoE footprint
hot expert reuse
long prefixes
capacity-led scale-out
Tool/RAG dominates
low reuse
random tiny reads
quality below threshold
POC sweep: model weights x TP/EP placement x context x concurrency x RAG payload x tool latency x reuse locality x cost/power

## Slide 10
Parallelism and Placement Change the Economics
The same model can look cheap or expensive depending on sharding, routing, and what stays resident.
v3 workload-fit
Use this slide to explain why the POC must sweep TP/EP, not freeze one topology too early.
Model footprint
Resident hot experts
Warm experts / KV
Cold or reusable state
Tensor parallel
Splits tensors across GPUs. Can reduce per-GPU weights, but adds cross-GPU communication and synchronization.
Expert parallel
Places different experts on different devices. Good when routing locality is stable; expensive when experts churn.
Tiered HBF placement
Keeps broad expert/KV portfolio near compute. Wins only when fetch/preload is hidden or cheaper than scale-out.
Question
Why it matters
External takeaway
What fits in GDDR?
If active weights/KV fit, GPU path can dominate.
Do not over-sell HBF for fit-in-memory workloads.
How stable is routing?
Hot experts favor cache/persistent tiers; churn hurts.
Ask for traces or generate realistic locality cases.
Can fetch overlap compute?
Peak bandwidth helps only if exposed stalls shrink.
Show latency stacks and queue curves.

## Slide 11
Break-Even Surface: Nonresident Bytes vs Reuse
v3 workload-fit
A break-even cell is where the complete service changes winner at fixed quality and SLO.
RTX/GPU
RTX+CXL
ATMOS/HBF
No-fit/measure
Low reuse
Some reuse
High reuse
Hot experts
Hot + long KV
Reuse and routing locality ->
Nonresident bytes / request
320 GB
NO-FIT?
CXL
ATMOS
ATMOS
ATMOS
160 GB
NO-FIT?
CXL
ATMOS
ATMOS
ATMOS
80 GB
RTX
CXL
CXL
ATMOS
ATMOS
40 GB
RTX
RTX
CXL
CXL
ATMOS
20 GB
RTX
RTX
RTX
CXL
CXL
Break-even logic
HBF helps when avoided reload/recompute and reduced scale-out exceed HBF path latency, software overhead, power, and cost. Higher reuse moves right. Larger nonresident working set moves up.

## Slide 12
Capacity Curve: Where the SLO Breaks
Illustrative queue-and-latency knee. Replace with real low, target, and saturation results.
v3 workload-fit
The winner is the highest accepted arrival rate before quality, latency, or queue depth violates the SLO.
Arrival rate / loan packages per hour
p95 latency / queue pressure
SLO boundary
RTX/GPU
RTX+CXL
ATMOS/HBF
No-fit/measure
Decision readout
Report low, target, burst, and saturation points. Show not just average throughput, but p95/p99 latency, queue growth, correctness pass rate, and failure/fallback behavior.

## Slide 13
CUSTOMER VALUE
ATMOS targets infrastructure cost and engineering effort together
1
Fewer capacity-driven shards
Potentially reduce accelerator slots, hosts and interconnect required only to make the model fit.
2
Less distributed-serving work
Reduce topology-specific sharding, communication tuning, regression testing and recovery logic.
3
More useful memory headroom
Reserve the fastest working tier for active KV and execution rather than static model capacity.
4
A lower-overhead path to scale
Evaluate rack power, cooling, network traffic and deployment steps per useful workload.
Customer-owned decision scorecard
$/useful token
Infrastructure economics
p99 / TTFT
Customer experience
Tokens / rack
Capacity efficiency
Watts / token
Energy efficiency
Steps / release
Engineering effort
[Confidential]
©2026 SANDISK CORPORATION OR ITS AFFILIATES
Illustrative — validate against customer workload and approved product configuration.
07

## Slide 14
CUSTOMER DISCOVERY
The right ATMOS evaluation starts with your constraint
These questions combine the strongest discovery material from both presentations.
Your workload
1
Which models, precisions, context lengths and concurrency levels matter?
2
Where do repeated prompts, documents or agent context create reuse?
3
Which flows are interactive versus batch / queue-based?
Your platform
1
Which OEM, accelerator, OS and inference engine are in production?
2
Where do sharding, networking or cache management create friction?
3
What power, cooling, rack and edge limits apply?
Your decision
1
Which KPI wins: p99, goodput, $/token, footprint or time-to-deploy?
2
What security, support and open-source boundaries must be met?
3
What result would justify a controlled hardware evaluation?
Output: a shared problem statement, one high-value workload and objective POC success gates.
[Confidential]
©2026 SANDISK CORPORATION OR ITS AFFILIATES
Illustrative — validate against customer workload and approved product configuration.
08

## Slide 15
POTENTIAL POC
Evaluate one meaningful workload — side by side
Use simulation to narrow the design space, then calibrate against measured hardware and the customer serving stack.
Candidate use cases
1
Long-context RAG
Reusable policy, engineering or support knowledge.
2
Batch enrichment
High-volume document, log or record processing.
3
Agentic workflows
Repeated instructions, tools and shared context.
POC method
1
Baseline
Current trace, topology and cost inputs
2
Simulate
TokenSim sensitivity and crossover analysis
3
Validate
Matched serving run and instrumentation
4
Decide
Joint review of results and limitations
Joint scorecard
✓
Useful token throughput
✓
TTFT and p99 latency
✓
Watts per useful token
✓
Network / memory utilization
✓
Deployment and operational effort
Output: go / no-go decision + deployment blueprint
[Confidential]
©2026 SANDISK CORPORATION OR ITS AFFILIATES
Illustrative — validate against customer workload and approved product configuration.
09