## Slide 1
SANDISK / ATMOS
ENTERPRISE OFFERING PROPOSAL
Build an independent
MoE inference appliance.
Protect the customer’s GPU stack.
Compete on completed work, quality and cost.
LEAD OFFERING
Native
ATMOS
service
CPU host
E3.S modules
Full model runtime
One supported endpoint
Decision: fund one native product; gate three extensions.
10-slide decision deck • 6 technical / cost backup slides
01 OCT 2026
Notes: This is a proposed E3.S-based ATMOS enterprise portfolio, not an AWS EC2 offering or a shipping SanDisk price list. The user’s “EC2” has been interpreted as the E3.S module platform discussed. AWS EC2 appears only as a public pricing benchmark. Recommend complete native ATMOS model execution as the base, with optional GPU prefill, speculative drafting and whole-layer pipeline research. No real ATMOS silicon performance or validated selling price is available. First ten slides form the executive narrative; six appendix slides provide defensible calculations and source links. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable.

## Slide 2
SANDISK / ATMOS
ENTERPRISE DEMAND
Lloyds proves the demand—not ATMOS economics.
A public banking example, reported 29 January 2026. No customer hardware inventory is inferred.
[S1] Lloyds Banking Group, “AI-driven benefits”, 29 Jan 2026.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
02
20,000
colleagues using Athena
Internal knowledge assistant
66%
less average search time
Reported for Athena
~£50m
GenAI value in 2025
Group-wide value—not inference spend
THE ENTERPRISE PATTERN
Secure knowledge access and document workflows can reach enterprise scale.
OUR PROPOSED ENTRY POINT
Offer a private MoE pool for eligible document jobs; retain existing GPU applications.
The bank did not disclose its GPU count, token load or inference bill. Do not invent a savings baseline.
Notes: The actual public example is Lloyds Banking Group, not a claimed ATMOS customer. Its January 2026 release reports Athena serving 20,000 colleagues, 66% lower search time, more than 50 GenAI deployments in 2025 and about £50m of GenAI value across the group. Do not equate value with hardware or inference savings. The proposed ATMOS workload later in the deck is a synthetic bank-scale pilot, not Lloyds traffic. Retrieval/indexing and business decision logic remain outside the ATMOS model-serving scope. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S1] Lloyds Banking Group — AI-driven benefits in 2025 https://www.lloydsbankinggroup.com/media/press-releases/2026/lloyds-banking-group/ai-driven-benefits-2026.html 29 January 2026. Around £50m GenAI value in 2025; >50 solutions; Athena used by 20,000 colleagues and search time reduced by 66%. Does not disclose GPU inventory, model architecture, requests, token volume or inference costs.

## Slide 3
SANDISK / ATMOS
PORTFOLIO
One common runtime. Four enterprise offerings.
Packaging options share the ATMOS runtime; execution boundaries and validation effort differ.
All four are proposals. Native runtime maturity is the common dependency. [S10–S12, S15]
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
03
A
Native MoE appliance
Complete requests → ATMOS
Private API, batch/economy jobs, isolated model pools.
LEAD • lowest customer coupling
B
Prefill / decode appliance
GPU prefill → KV → ATMOS decode
Add GPU prefill only when native prefill limits the service.
CONDITIONAL • KV interoperability
C
Speculative inference node
Small GPU drafter → ATMOS verifier
Seek more accepted target tokens per verification cycle.
RESEARCH • acceptance + rollback
D
Whole-layer pipeline node
GPU stage → ATMOS stage
Few stage crossings rather than one crossing at every FFN.
DEFER • heterogeneous scheduling
Notes: These are four proposed products/architectures; they are not validated ATMOS features. A is complete native inference and can be delivered as a separate appliance or a dedicated pool in the customer’s Kubernetes cluster. B retains a complete model in GPU prefill as well as on the native ATMOS decoder; no free GPU-weight-reclamation claim. C uses an auxiliary draft model and an ATMOS MoE target; correctness requires target-distribution-preserving verification, not majority voting. D assigns complete contiguous layer groups, including their attention/KV, to devices; pipeline fill and balance remain risks. A service with lower TTFT demands is not necessarily cheap unless matched GPU batch serving also loses. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S10] Tenstorrent — vLLM TT plugin https://github.com/tenstorrent/vllm-tt-plugin Public precedent for a platform plugin containing model loading, worker execution and scheduling. It does not establish full native ATMOS model support. Pin exact releases and qualify the specific ATMOS target. [S11] NVIDIA Dynamo — disaggregated serving https://docs.nvidia.com/dynamo/components/router/disaggregated-serving Independent prefill/decode pools and KV handoff. Does not itself supply an ATMOS decoder or arbitrary cross-accelerator KV compatibility. [S12] Leviathan et al. — speculative decoding, ICML 2023 https://proceedings.mlr.press/v202/leviathan23a.html Draft-and-target verification algorithm. Distribution preservation requires the correct acceptance/correction procedure. No ATMOS speedup is supplied by this paper. [S15] vLLM — parallelism and scaling https://docs.vllm.ai/en/latest/serving/parallelism_scaling/ Public layer/pipeline parallelism precedent; not a ready-made heterogeneous GPU/ATMOS implementation.

## Slide 4
SANDISK / ATMOS
LEAD ARCHITECTURE
Integrate at the request boundary—not inside GPU execution.
The native ATMOS service owns attention, KV, router, experts and output for every assigned request.
Proposed design. [S10] TT platform-plugin precedent—not ATMOS certification. [S14] Kubernetes allocation.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
04
Existing AI gateway / job policy
Existing NVIDIA / AMD service
GPU runtime and model deployment remain unchanged
New ATMOS-native MoE service
Native prefill + decode • ATMOS-owned active KV
Interactive / unsupported requests
Eligible model + context + deadline
Deploy A: separate appliance / cluster
Deploy B: dedicated nodes in existing K8s
Notes: Route each production request to exactly one eligible complete serving endpoint. No blind forking to both GPU and ATMOS; use duplicated traffic only for a controlled shadow evaluation. Adding an endpoint requires gateway or application configuration—this is not literally zero integration. Separate appliance is preferred for a certified turnkey GPU deployment. Shared-cluster packaging adds ATMOS driver, device plugin, operator and readiness management but does not modify GPU model execution. Do not equate one module with one serving Pod: one complete model may need several devices. The native ATMOS runtime, not labels, must implement attention/KV/full-model execution. Active KV does not move between GPU and ATMOS in offering A. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S10] Tenstorrent — vLLM TT plugin https://github.com/tenstorrent/vllm-tt-plugin Public precedent for a platform plugin containing model loading, worker execution and scheduling. It does not establish full native ATMOS model support. Pin exact releases and qualify the specific ATMOS target. [S14] Kubernetes — device plugins https://kubernetes.io/docs/concepts/extend-kubernetes/compute-storage-net/device-plugins/ Device discovery/resource advertisement and allocation. Pod labels are not hardware allocation or proof that a complete model is ready.

## Slide 5
SANDISK / ATMOS
OEM REFERENCE DESIGN
Specify an ATMOS-first node. Do not pre-buy GPUs.
OEM design study: one CPU host + eight E3.S modules. All ATMOS values remain unqualified targets.
[S6] AMD EPYC 9355P. [I1] Internal ATMOS envelope. Chassis, routing and working-memory budgets are proposed.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
05
HOST + SERVICE PLANE
1 × EPYC 9355P reference CPU
32 cores • PCIe 5.0 ×128 • 12 DDR5 channels
384 GB host DDR5 (12 × 32 GB)
2 × 3.84 TB mirrored NVMe
Dual 100 GbE service / management path
OEM-sized chassis, BMC and redundant power
Host DRAM is not automatically NPU KV memory
ATMOS EXECUTION PLANE
8 × E3.S NPU + HBF + LPDDR
A0
A1
A2
A3
A4
A5
A6
A7
1,024 GB HBF nominal; 800 GB study budget
128 GB LPDDR at 16 GB/module target
2 × (Gen5 x16 → 4 × Gen5 x4) domains
Native inter-device collectives must be qualified.
Two branches ≠ automatic HA or fabric bandwidth.
Notes: The CPU reference is a real public part. The server configuration is a proposed design, not an OEM quote or validated BOM. EPYC 9355P official specs: 32 cores, 280W, 128 PCIe Gen5 lanes and 12 memory channels. Proposed 384GB host memory uses one 32GB DIMM per channel; memory speed is OEM-dependent. Two four-endpoint branches each use 16 upstream+16 downstream switch port-lanes; together they consume 32 host lanes, so do NOT claim host-lane savings relative to 8 direct x4 devices. They are candidate locality/management domains; different switches may be required from the older 48-lane eight-device branch. The host service network is not asserted to be the native NPU collective fabric. Nominal HBF 8×128GB, application planning allocation 8×100GB; select the 16GB/module LPDDR target for this study, not the lower 8GB variant. 96GB aggregate LPDDR after a provisional 4GB/device reserve is a planning ledger, not unified memory. Full-model compute including attention/KV is unqualified. No NPU TOPS-to-throughput conversion is used. Power 1.6kW is used ONLY as a later TCO sensitivity input, not a specification. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S6] AMD EPYC 9355P — official specifications https://www.amd.com/en/products/processors/server/epyc/9005-series/amd-epyc-9355p.html 32 cores; 280W default TDP; 1 socket; PCIe 5.0 x128; 12 DDR5 channels. This is a host CPU reference, not an ATMOS-compatible server certification. [I1] Supplied ATMOS proposal — internal, unqualified device targets User-supplied private proposal ATMOS_MoE_Hybrid_Switched_E3S_Final_Proposal_v1.docx, reference resource envelope (page 2 in supplied extraction). Up to 128GB HBF, 100GB application planning budget/device, 8–16GB LPDDR, ~200GB/s local HBF read target, Gen5/Gen6 x4 candidates. No validated NPU service rate, native runtime support, price, power or production date.

## Slide 6
SANDISK / ATMOS
MODEL ENVELOPE
Model capacity is knowable. Service throughput is not yet known.
Full-model raw weights, not only routed experts. FP8 = 1 byte/parameter; 16-bit = 2 bytes/parameter.
[S2–S5] Publisher model cards/configs. Calculated raw bytes exclude scales, packing, replicas and runtime memory.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
06
Model / role
Total / active
Routed experts
Raw FP8 / 16-bit
100-GB HBF minimum*
Qwen3-30B-A3B
Bring-up / smaller service
30.5B / 3.3B
128; top-8
48 layers
30.5 / 61 GB
1 / 1 modules
Qwen3-235B-A22B
Commercial study target
235B / 22B
128; top-8
94 layers
235 / 470 GB
3 / 5 modules
DeepSeek-V3
Large-model expansion
671B / 37B
256 + shared; top-8
58 MoE + 3 dense layers
671 / 1,342 GB
7 / 14 modules
Qwen 235B: 32 × 8K sequences need 47 GiB of KV
Logical BF16 cache; validate per-device layouts and working-memory reserve.
*Capacity floor only
Not a validated serving-group size.
Notes: The minimum HBF module count is ceil(full-model raw bytes/100GB). It is not a device-count recommendation: actual NPU speed, local KV, compiler layouts, replication, per-device memory and interconnect determine grouping. All-FP8 and all-16-bit arithmetic is a capacity screen; actual checkpoints can use mixed precision and scales. Qwen235 BF16 logical KV = 2×94×4×128×2 bytes×8192 tokens = 1.46875 GiB/sequence; 32 sequences = 47 GiB (50.465865728 decimal GB). Qwen30 similarly gives 0.75 GiB/sequence. DeepSeek uses MLA and must not be estimated using the Qwen GQA cache formula. Native DeepSeek 16-bit full weights exceed an eight-device 800GB study allocation; 14 is a raw capacity floor, not a supported mesh. Public parameter counts are rounded. Total context includes prompt and generated tokens. Different models need separate quality evaluation. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S2] Qwen3-30B-A3B — publisher model card https://huggingface.co/Qwen/Qwen3-30B-A3B 30.5B total, 3.3B activated, 128 experts, top-8. A separate model/quality qualification, not a substitute asserted equivalent to 235B. [S3] Qwen3-30B-A3B — configuration https://huggingface.co/Qwen/Qwen3-30B-A3B/blob/main/config.json 48 layers, 4 KV heads, head dimension 128. Source for logical BF16 KV calculations. [S4] Qwen3-235B-A22B — model and configuration https://huggingface.co/Qwen/Qwen3-235B-A22B/blob/main/config.json Model card: https://huggingface.co/Qwen/Qwen3-235B-A22B . Approximately 235B total, 22B active; 94 layers, 128 experts, top-8, 4 KV heads, head dimension 128. [S5] DeepSeek-V3 — model and configuration https://huggingface.co/deepseek-ai/DeepSeek-V3/blob/main/config.json Model card: https://huggingface.co/deepseek-ai/DeepSeek-V3 . Approximately 671B total, 37B activated, 61 layers, first 3 dense, 256 routed and 1 shared expert per MoE layer. MLA cache is implementation-specific. [I1] Supplied ATMOS proposal — internal, unqualified device targets User-supplied private proposal ATMOS_MoE_Hybrid_Switched_E3S_Final_Proposal_v1.docx, reference resource envelope (page 2 in supplied extraction). Up to 128GB HBF, 100GB application planning budget/device, 8–16GB LPDDR, ~200GB/s local HBF read target, Gen5/Gen6 x4 candidates. No validated NPU service rate, native runtime support, price, power or production date.

## Slide 7
SANDISK / ATMOS
BANK-SCALE PILOT DESIGN
Start with a bounded document workload—not “all bank AI.”
Synthetic sizing anchored on a 20,000-user scale. These are not Lloyds workloads or measured rates.
[S1] Public user-scale anchor only. All activity, traffic, model and service assumptions on this slide are proposed.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
07
20,000
user population
40% × 6
daily-active share × calls
48,000
model calls per day
TRAFFIC ASSUMPTIONS
8-hour service window → 1.67 RPS mean
3× peak → 5 RPS across all work
40% eligible → 19,200 jobs/day; 2 RPS peak
FIRST QUALIFICATION PROFILE
Qwen3-235B; one approved FP8 pack
4,096 input / up to 512 output tokens; 8K cap
p95 completion ≤120 s; no streaming SLO
Factuality + extraction quality must pass
Notes: Arithmetic: 20,000×0.4×6=48,000 calls/day. Over 8×3600 seconds =1.6667 RPS average; 3× peak =5 RPS. The proposed eligible fraction is 0.4, yielding 19,200 calls/day, 0.6667 average RPS and 2 peak RPS. Target requests are candidate document summaries, extraction and controlled drafting; no autonomous credit, claims or underwriting decisions are proposed. The example does not replace Athena, its retrieval pipeline or its model with a claim of equal quality. Specify real prompt/output distributions, 15-minute bursts, tenant policy, error rates and N+1 capacity in pilot. Candidate native batch deadline is p95 120 seconds including queue/prefill/decode; log TTFT/TPOT diagnostically rather than promise an interactive-token SLA. No disclosed public rate supports a specific device count. Section backup reverse-sizes hypothetical throughput outcomes. A business-window workload can favor elastic GPU cloud economics; the cost gate must reflect actual billed hours. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S1] Lloyds Banking Group — AI-driven benefits in 2025 https://www.lloydsbankinggroup.com/media/press-releases/2026/lloyds-banking-group/ai-driven-benefits-2026.html 29 January 2026. Around £50m GenAI value in 2025; >50 solutions; Athena used by 20,000 colleagues and search time reduced by 66%. Does not disclose GPU inventory, model architecture, requests, token volume or inference costs. [S4] Qwen3-235B-A22B — model and configuration https://huggingface.co/Qwen/Qwen3-235B-A22B/blob/main/config.json Model card: https://huggingface.co/Qwen/Qwen3-235B-A22B . Approximately 235B total, 22B active; 94 layers, 128 experts, top-8, 4 KV heads, head dimension 128.

## Slide 8
SANDISK / ATMOS
PUBLISHED COST CONTROLS
Use real price anchors—and include a cheaper small-model control.
Compute prices checked 1 October 2026. Annual figures = current hourly rate × 8,760 hours, not a contract.
[S7] Lambda instance pricing. [S8–S9] AWS Capacity Blocks/specs. Taxes, support, egress and future price changes excluded.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
08
LAMBDA • QWEN 235B CANDIDATE
4 × H100 SXM
$16.36/h
$143,314 / year
320 GB aggregate GPU memory
900 GiB host RAM
$4.09 per GPU-hour
Weight/KV fit and service rate must be tested.
AWS P5.48XLARGE • CAPACITY BLOCK
8 × H100
$41.528/h
$363,785 / year
640 GB aggregate GPU memory
2 TiB host RAM
US East (N. Virginia)
Reservation rate—not On-Demand pricing.
LAMBDA • SMALL-MODEL CONTROL
1 × GH200
$2.29/h
$20,060 / year
96 GB GPU memory
432 GiB host RAM
Candidate for Qwen 30B
Do not use an eight-GPU control for every model.
Notes: Published price snapshot, not price recommendations or available capacity guarantees. Lambda 4×H100 SXM price is $4.09 per GPU per hour; group rate = $16.36; annual 8,760-hour amount $143,313.60; 3-year static amount $429,940.80. AWS p5.48xlarge Capacity Block in N. Virginia is $41.528 per instance-hour; annual $363,785.28. AWS announces $5.970 per P5 accelerator-hour effective 7 October 2026; 8 GPUs would then be $47.760/hour. Neither AWS rate is On-Demand or a three-year promise. Lambda single GH200 96GB at $2.29/hour gives $20,060.40/year; all-three hardware offerings are not equal performance units. Qwen235 FP8 235GB raw plus KV, scales and workspace makes 4 H100 a candidate capacity screen, not validated serving support. Establish actual fit before using it as the benchmark. Include purchased/on-prem GPU and vendor quotes for formal TCO. AMD GPU system price is quote-required; do not invent a number. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S7] Lambda — public instance price list https://lambda.ai/pricing Snapshot 1 October 2026: 4x H100 SXM = $4.09/GPU-hour ($16.36/group-hour), 80GB/GPU; 900GiB host RAM. Single GH200 $2.29/hour (96GB). Single A10 $1.29/hour (24GB). 8x B200 $6.69/GPU-hour. Taxes extra; availability and negotiated pricing differ. [S8] AWS EC2 Capacity Blocks — public pricing https://aws.amazon.com/ec2/capacityblocks/pricing/ Snapshot 1 October 2026: p5.48xlarge N. Virginia $41.528/instance-hour (8 H100); p5.4xlarge $5.191. These are Capacity Block reservation rates, NOT On-Demand. AWS announces P5 $5.970/accelerator-hour effective 7 October 2026. Static annualization is not a three-year quote. [S9] AWS — accelerated instance specifications https://aws.amazon.com/ec2/instance-types/accelerated-computing/ P5.48xlarge: 8 H100, 640GB HBM3, 192 vCPU, 2TiB host memory, up to 3200Gbps EFAv2. P5.4xlarge: one H100, 80GB, 16vCPU, 256GiB; GPU Direct RDMA not supported on p5.4xlarge.

## Slide 9
SANDISK / ATMOS
DESIGN-TO-COST GATE
At an $80k node target, ATMOS must earn its economics.
Qwen 235B study: compare the same model, quality, deadline and accepted output—not raw memory capacity.
Calculated from [S7] + explicit ATMOS budget assumptions. No measured ATMOS rate or vendor quote is available.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
09
$80k
appliance purchase target
Design-to-cost allowance; not a selling price
$141k
3-year modeled node cost
Includes support, facility/admin and energy
≥44%
of 4-H100 accepted rate
For ≥25% lower cost/accepted unit*
THE TESTABLE HURDLE
Break-even: native rate >33% of the
4-H100 control at the same service contract.
THE LOW-UTILIZATION WARNING
At 2,080 billed hours/year, the GPU control
is ~$102k over 3 years—below $141k.
*Unit-cost screen before failure-reserve effects and migration NRE. A node is not assumed equivalent to a GPU group.
Notes: All ATMOS economic inputs are proposed, not quoted. Purchase budget $80,000, annual support 15% of purchase ($12,000), site/network/admin allowance $6,000 per year, whole-node IT draw 1.6kW, PUE1.4, electricity $0.12/kWh, 8,760 hours/year, 3-year horizon, no residual value. Electricity =1.6×1.4×0.12×8760=$2,354.688/year. Three-year native TCO=80,000+36,000+18,000+7,064.064=$141,064.064. 4-H100 Lambda static 24/7 compute cost=$429,940.8 over three years. Unit-cost break-even rate ratio=141064.064/429940.8=0.328101. For 25% lower unit cost require qA/qG≥0.437468. With 2,080 billed GPU hours/year, control compute cost=$102,086.40/3years, lower than proposed native TCO at the same serving rate. Same-rate cloud hours break-even ~2,874/year. Do not book sunk GPU purchases as cash savings, do not add node and constituent GPU savings, and do not assume data privacy makes cloud legally forbidden. Formal release requires same service/availability and priced operating scope. Gross margin and manufacturing feasibility are not established by an $80k design allowance. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S7] Lambda — public instance price list https://lambda.ai/pricing Snapshot 1 October 2026: 4x H100 SXM = $4.09/GPU-hour ($16.36/group-hour), 80GB/GPU; 900GiB host RAM. Single GH200 $2.29/hour (96GB). Single A10 $1.29/hour (24GB). 8x B200 $6.69/GPU-hour. Taxes extra; availability and negotiated pricing differ. [I1] Supplied ATMOS proposal — internal, unqualified device targets User-supplied private proposal ATMOS_MoE_Hybrid_Switched_E3S_Final_Proposal_v1.docx, reference resource envelope (page 2 in supplied extraction). Up to 128GB HBF, 100GB application planning budget/device, 8–16GB LPDDR, ~200GB/s local HBF read target, Gen5/Gen6 x4 candidates. No validated NPU service rate, native runtime support, price, power or production date.

## Slide 10
SANDISK / ATMOS
DECISION / 10-MINUTE DISCUSSION
Approve one native product path.
Gate every extension on evidence.
1
MODEL
Simulator
Native attention + KV
Experts + contention
Feasibility envelope
2
SOFTWARE
Emulator
Complete model/API
GPU surrogate + errors
No ATMOS speed claim
3
SILICON
Physical node
Eight E3.S + host
Power, latency, quality
Real cost / throughput
4
CUSTOMER
Pilot release
Bank trace + reserve
Install / recover / update
Reconciled economics
OWNERS
SanDisk: service & product | Tenstorrent: native runtime | OEM: node & lifecycle
Request: one runtime commitment, one OEM design study, one customer workload—not a launch promise.
STOP if native attention/KV, complete-model performance, physical integration or matched-cost economics fails.
Internal proposal • candidate partners are not commitments. [S10, S13] | Technical and cost backup follows.
10
Notes: Approval sought is for a bounded native MoE feasibility and OEM design program, not product launch. Simulator and functional emulator can proceed in parallel after the common model and interface contracts are fixed; the diagram is evidence progression, not a requirement to serially wait for each team. Emulator GPU timings are not ATMOS projections. An optional FPGA can exercise endpoint contracts but does not certify actual silicon; CXL memory alone is not an NPU emulator. The physical node is now an ATMOS-first native service, not the prior eight-RTX/eight-ATMOS layer-offload product. Suggested OEM inquiry: Supermicro modular DCBBS; a second OEM can be selected by actual design support. Sandisk must own model service QA, admission/security/readiness/telemetry, support, and truthful economics. Tenstorrent must commit to the exact model/precision, full attention/KV, supported mesh, native prefill/decode, shape/concurrency and release matrix. Public plugin precedent is not that commitment. Existing GPU engines remain unchanged for offering A. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S10] Tenstorrent — vLLM TT plugin https://github.com/tenstorrent/vllm-tt-plugin Public precedent for a platform plugin containing model loading, worker execution and scheduling. It does not establish full native ATMOS model support. Pin exact releases and qualify the specific ATMOS target. [S13] Supermicro — Data Center Building Block Solutions https://www.supermicro.com/en/solutions/dcbbs Public modular infrastructure/OEM-integration capability; a reason for engagement, not a partnership or an ATMOS design commitment.

## Slide 11
SANDISK / ATMOS
BACKUP A / EXTENSION BOUNDARIES
The three extensions buy different benefits—and different obligations.
None is a gateway-only feature. GPU cloud prices below are budgeting proxies, not OEM hardware quotations.
[S7] Published GPU rates. [S11] Disaggregation. [S12] Speculative decoding. [S15] Pipeline parallelism.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
11
B PREFILL / DECODE
GPU prefill → KV handoff → ATMOS decode
4×H100 prefill reference (320 GB): $429,941 / 3 years, shared across n decoder groups. Requires a full decoder and compatible KV handoff; measure the split ratio.
C SPECULATIVE
Small GPU draft → token block → ATMOS verification
24-GB A10 draft reference: $1.29/h = $33,901 / 3 years. Needs >24% extra accepted output just to offset compute, plus correct verification and KV rollback.
D WHOLE-LAYER PIPELINE
GPU layer group → activation → ATMOS layer group
GPU count and spend depend on layer partition; price after memory fit. ATMOS owns attention/KV for its stages. Balance, microbatch flow and recovery remain unproven.
Notes: Cost notes: The $429,940.80 prefill GPU amount and $33,901.20 A10 amount are 3-year static 24/7 cloud-rental equivalents used only as budget anchors; a physically colocated OEM GPU requires a separate quotation. Do not infer that cloud prefill plus on-prem ATMOS is a qualified KV path. Allocating one prefill group across n decoders is accounting, not a proven sizing ratio. Extra drafting compute alone is 33,901.20 / 141,064.064 = 24.03% of the native-node budget, so accepted output must improve by more than that to lower unit cost before new development cost. NVIDIA and AMD GPU variants both require their own compatible handoff/backend tests. More precise boundaries: Offering B is a complete GPU prefill runtime plus complete ATMOS decoder and a state-handoff protocol. A normal chat-completion endpoint alone cannot export its KV; customer prefill configuration must allow the connector. LMCache/Dynamo/NIXL can support parts of management/transport but do not create ATMOS attention or native execution. Offering C drafts tokens, not hidden activations for every layer; target distribution preservation requires the cited accept/reject and correction rules. Acceptance rate, verification cost, and shared memory demand determine benefit; speculation can lose performance. Offering D places complete layer stages, not independent FFNs, so local KV follows stage ownership; multiple requests can fill the pipeline but single-request dependency remains. Direct P2P between ATMOS devices is a topology question in native execution, not inherited as unnecessary from the old FFN-only design. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S7] Lambda — public instance price list https://lambda.ai/pricing Snapshot 1 October 2026: 4x H100 SXM = $4.09/GPU-hour ($16.36/group-hour), 80GB/GPU; 900GiB host RAM. Single GH200 $2.29/hour (96GB). Single A10 $1.29/hour (24GB). 8x B200 $6.69/GPU-hour. Taxes extra; availability and negotiated pricing differ. [S11] NVIDIA Dynamo — disaggregated serving https://docs.nvidia.com/dynamo/components/router/disaggregated-serving Independent prefill/decode pools and KV handoff. Does not itself supply an ATMOS decoder or arbitrary cross-accelerator KV compatibility. [S12] Leviathan et al. — speculative decoding, ICML 2023 https://proceedings.mlr.press/v202/leviathan23a.html Draft-and-target verification algorithm. Distribution preservation requires the correct acceptance/correction procedure. No ATMOS speedup is supplied by this paper. [S15] vLLM — parallelism and scaling https://docs.vllm.ai/en/latest/serving/parallelism_scaling/ Public layer/pipeline parallelism precedent; not a ready-made heterogeneous GPU/ATMOS implementation.

## Slide 12
SANDISK / ATMOS
BACKUP B / MEMORY AND SERVICE BUDGETS
The native-product risk moves to attention, active KV and device fabric.
LPDDR is a working-memory budget. HBF residency is not sufficient to operate a complete model service.
[S3–S5] Model configurations. [I1] Internal memory targets. All budgets/calculations must be checked per device.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
12
Qwen BF16 KV
Per 8K sequence
32 sequences
Implication
30B-A3B: 48 layers
0.750 GiB
24.0 GiB
Smaller complete-model bring-up; quality must be qualified.
235B-A22B: 94 layers
1.469 GiB
47.0 GiB
~50.47 decimal GB; cannot be treated as one shared pool.
235B at 32K context
5.875 GiB
188.0 GiB
Exceeds 8 × 16GB nominal LPDDR before any reserve.
PROPOSED 16-GB/MODULE STUDY
8 × (16 − 4) GB = 96 GB aggregate
Remaining local memory must fit KV + transient state.
DO NOT INHERIT THE OLD P2P ASSUMPTION
A native multi-device model may need collectives.
Qualify the real path, bandwidth and synchronization.
Notes: Logical KV formula for these GQA Qwen models: 2(K and V)×layer count×KV heads×head dimension×bytes×total cached tokens. Qwen30: 2×48×4×128×2×8192=805,306,368 bytes=0.75GiB. Qwen235: 2×94×4×128×2×8192=1,577,058,304 bytes=1.46875GiB. Multiply by32 sequences: 47GiB. At32768 total tokens, multiply by4=188GiB for32 sequences. This exceeds128 decimalGB nominal LPDDR=119.21GiB. Provisional per-device12GB working budget leaves aggregate96GB=89.4GiB, but actual per-layer/head/TP/PP assignment can replicate state and scratch may be larger. Cache layouts, FP8 KV, sliding attention and MLA cannot be substituted without model/runtime evidence. Host DDR memory does not cure a missing NPU memory interface. Native HBF feed must distinguish controller/media bandwidth from actual NPU-consumed bytes. Large batches may activate most experts, and slowest required work can dominate tail latency. Do not infer native tokens/s from the older ambiguous 64 TOPS/TFLOPS label. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S3] Qwen3-30B-A3B — configuration https://huggingface.co/Qwen/Qwen3-30B-A3B/blob/main/config.json 48 layers, 4 KV heads, head dimension 128. Source for logical BF16 KV calculations. [S4] Qwen3-235B-A22B — model and configuration https://huggingface.co/Qwen/Qwen3-235B-A22B/blob/main/config.json Model card: https://huggingface.co/Qwen/Qwen3-235B-A22B . Approximately 235B total, 22B active; 94 layers, 128 experts, top-8, 4 KV heads, head dimension 128. [S5] DeepSeek-V3 — model and configuration https://huggingface.co/deepseek-ai/DeepSeek-V3/blob/main/config.json Model card: https://huggingface.co/deepseek-ai/DeepSeek-V3 . Approximately 671B total, 37B activated, 61 layers, first 3 dense, 256 routed and 1 shared expert per MoE layer. MLA cache is implementation-specific. [I1] Supplied ATMOS proposal — internal, unqualified device targets User-supplied private proposal ATMOS_MoE_Hybrid_Switched_E3S_Final_Proposal_v1.docx, reference resource envelope (page 2 in supplied extraction). Up to 128GB HBF, 100GB application planning budget/device, 8–16GB LPDDR, ~200GB/s local HBF read target, Gen5/Gen6 x4 candidates. No validated NPU service rate, native runtime support, price, power or production date.

## Slide 13
SANDISK / ATMOS
BACKUP C / COST AUDIT
The $141k native-node case is a budget—not a SanDisk quotation.
Three-year model; USD; no residual value. Comparable service performance is still unknown.
Sources: [S7] cloud compute rates. All ATMOS prices, support, power, PUE and site/admin costs are assumptions.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
13
Native cost input
Basis
3-year total
ATMOS modules + OEM host/fabric
$80,000 target
$80,000
Support / runtime maintenance
15% capex / yr
$36,000
Site / network / admin allowance
$6,000 / yr
$18,000
Energy: 1.6kW × 1.4 × $0.12/kWh
8,760h / yr
$7,064
TOTAL
$47,021 / yr
$141,064
CAPEX SENSITIVITY
$60k → $112k TCO
$80k → $141k TCO
$120k → $199k TCO
Break-even rate vs 4 H100:
26% / 33% / 47%, respectively.
Design allowance: $60k for 8 modules + $20k host/fabric. Both need supplier cost validation.
Excluded: taxes, financing, common application services, product R&D and customer-specific migration.
Illustrative fleet model adds $100k migration NRE separately. Include these in a commercial quote.
Notes: Exact calculations are audited in calculations.json used to build this deck. Native total=capex×(1+3×supportfraction)+3×(site/admin+ITkW×PUE×electricity×8760). At P=$80k: P×1.45+3×(6000+2354.688)=141064.064. Per-module $7,500 allocation and $20,000 OEM host/fabric allocation are design-to-cost targets, not current costs or intended list prices. At $60k total112064.064; at$120k total199064.064. Rate thresholds vs4-H100 cost429940.8 are26.065%,32.810%,46.300%. Table rounds thresholds upward for ease of review. Hardware gross margin, OEM integration NRE, multiyear price changes and institutional discounts remain unknown. Holding all else constant, if native reaches50% of control rate and target25% lower unit cost, allowable native capex≈$93,906 under this model. This is a buying/design threshold, not a prediction. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S7] Lambda — public instance price list https://lambda.ai/pricing Snapshot 1 October 2026: 4x H100 SXM = $4.09/GPU-hour ($16.36/group-hour), 80GB/GPU; 900GiB host RAM. Single GH200 $2.29/hour (96GB). Single A10 $1.29/hour (24GB). 8x B200 $6.69/GPU-hour. Taxes extra; availability and negotiated pricing differ. [I1] Supplied ATMOS proposal — internal, unqualified device targets User-supplied private proposal ATMOS_MoE_Hybrid_Switched_E3S_Final_Proposal_v1.docx, reference resource envelope (page 2 in supplied extraction). Up to 128GB HBF, 100GB application planning budget/device, 8–16GB LPDDR, ~200GB/s local HBF read target, Gen5/Gen6 x4 candidates. No validated NPU service rate, native runtime support, price, power or production date.

## Slide 14
SANDISK / ATMOS
BACKUP D / REVERSE-SIZING
The same bank pilot can be a win—or a NO-GO.
Illustration only: 2 RPS peak; GPU control assumed 0.50 RPS per 4-H100 group; one full group in reserve.
Hypothetical service rates—not benchmarks. [S7] static cloud prices + Backup C assumptions; includes $100k ATMOS migration.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
14
Candidate outcome
Qualified RPS*
Units incl. reserve
3-year cost
vs GPU control
4-H100 control
0.50 / group
5 groups = 20 GPUs
$2.150m
Reference
ATMOS: fails economics
0.125 / node
17 nodes / 136 E3.S
$2.498m
16% MORE
ATMOS: conditional case
0.25 / node
9 nodes / 72 E3.S
$1.370m
36% LOWER
ATMOS: stronger case
0.50 / node
5 nodes / 40 E3.S
$0.805m
63% LOWER
Required units = 1 + ceil(peak RPS / measured RPS per complete serving unit).
*Each rate must meet identical model quality, 8K context cap and p95 completion ≤120s.
24/7 static rental comparison only; elastic or purchased-GPU controls can change the result substantially.
Notes: This is a reverse-sizing experiment, not a forecast and not the public bank’s infrastructure. Given demandR=2RPS and controlqG=.5RPS/group, NG=1+ceil(2/.5)=5. Atmqa values .125/.25/.5 produce17/9/5 nodes, respectively. Controls cost5×429940.8=$2,149,704. Atm costs N×141064.064+$100,000 migration: $2,498,089.088 / $1,369,576.576 / $805,320.32. Changes +16.206%, -36.290%, -62.538%. Reserve covers loss of one complete serving unit only, not an entire multi-node rack or site. Local module replicas are not equivalent to node failure tolerance. Same unit counts are not equal throughput unless measured q is valid; a slow ATMOS unit may require a larger fleet. More than32 active8K sequences may exceed the working-memory profile, so performance testing must include actual service times and queueing. For a business-window workload, compare elastic billed hours and idle shutdown costs before any claim. This table is deliberately able to say NO-GO. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S7] Lambda — public instance price list https://lambda.ai/pricing Snapshot 1 October 2026: 4x H100 SXM = $4.09/GPU-hour ($16.36/group-hour), 80GB/GPU; 900GiB host RAM. Single GH200 $2.29/hour (96GB). Single A10 $1.29/hour (24GB). 8x B200 $6.69/GPU-hour. Taxes extra; availability and negotiated pricing differ.

## Slide 15
SANDISK / ATMOS
BACKUP E / SOURCE REGISTER
Sources: public evidence and model geometry.
Clickable source titles. Numerical assumptions are documented separately; no public ATMOS benchmark is asserted.
Sources reviewed 1 October 2026. Full scope, caveats and URLs also appear in speaker notes.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
15
S1
Lloyds Banking Group — AI-driven benefits in 2025
Public enterprise adoption and value; not a GPU-cost disclosure.
S2
Qwen3-30B-A3B — publisher model card
Model size and sparse architecture; separate quality target from the 235B model.
S3
Qwen3-30B-A3B — configuration
Cache geometry for the 30B memory calculation.
S4
Qwen3-235B-A22B — model and configuration
235B model card + config: raw weights and GQA KV calculation.
S5
DeepSeek-V3 — model and configuration
671B total / 37B active; MLA needs a backend-specific state calculation.
S6
AMD EPYC 9355P — official specifications
Real CPU specification; the proposed ATMOS OEM box is not certified.
I1
Supplied ATMOS proposal — internal, unqualified device targets
Supplied v1 proposal, resource envelope: HBF / LPDDR / links are planning targets.
Notes: Source-derived data must be distinguished from proposal data. I1 is a user-supplied confidential planning document, not a public release. Its HBF and LPDDR budgets are inherited as targets only. Definitions: published = vendor/publisher documented; calculated = direct arithmetic from declared inputs; proposed = design/workload/cost assumption; measured = an identified physical benchmark. This deck contains no new measured ATMOS results. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S1] Lloyds Banking Group — AI-driven benefits in 2025 https://www.lloydsbankinggroup.com/media/press-releases/2026/lloyds-banking-group/ai-driven-benefits-2026.html 29 January 2026. Around £50m GenAI value in 2025; >50 solutions; Athena used by 20,000 colleagues and search time reduced by 66%. Does not disclose GPU inventory, model architecture, requests, token volume or inference costs. [S2] Qwen3-30B-A3B — publisher model card https://huggingface.co/Qwen/Qwen3-30B-A3B 30.5B total, 3.3B activated, 128 experts, top-8. A separate model/quality qualification, not a substitute asserted equivalent to 235B. [S3] Qwen3-30B-A3B — configuration https://huggingface.co/Qwen/Qwen3-30B-A3B/blob/main/config.json 48 layers, 4 KV heads, head dimension 128. Source for logical BF16 KV calculations. [S4] Qwen3-235B-A22B — model and configuration https://huggingface.co/Qwen/Qwen3-235B-A22B/blob/main/config.json Model card: https://huggingface.co/Qwen/Qwen3-235B-A22B . Approximately 235B total, 22B active; 94 layers, 128 experts, top-8, 4 KV heads, head dimension 128. [S5] DeepSeek-V3 — model and configuration https://huggingface.co/deepseek-ai/DeepSeek-V3/blob/main/config.json Model card: https://huggingface.co/deepseek-ai/DeepSeek-V3 . Approximately 671B total, 37B activated, 61 layers, first 3 dense, 256 routed and 1 shared expert per MoE layer. MLA cache is implementation-specific. [S6] AMD EPYC 9355P — official specifications https://www.amd.com/en/products/processors/server/epyc/9005-series/amd-epyc-9355p.html 32 cores; 280W default TDP; 1 socket; PCIe 5.0 x128; 12 DDR5 channels. This is a host CPU reference, not an ATMOS-compatible server certification. [I1] Supplied ATMOS proposal — internal, unqualified device targets User-supplied private proposal ATMOS_MoE_Hybrid_Switched_E3S_Final_Proposal_v1.docx, reference resource envelope (page 2 in supplied extraction). Up to 128GB HBF, 100GB application planning budget/device, 8–16GB LPDDR, ~200GB/s local HBF read target, Gen5/Gen6 x4 candidates. No validated NPU service rate, native runtime support, price, power or production date.

## Slide 16
SANDISK / ATMOS
BACKUP F / SOURCE REGISTER
Sources: pricing, execution and delivery interfaces.
Price snapshots require revalidation at purchase. Framework capabilities do not establish ATMOS compatibility.
Sources reviewed 1 October 2026. AWS announces a P5 Capacity Block price change effective 7 October 2026.
INTERNAL CONCEPT • 01 OCT 2026 • NOT A PRODUCT OR PERFORMANCE COMMITMENT
16
S7
Lambda — public instance price list
lambda.ai/pricing
S8
AWS EC2 Capacity Blocks — public pricing
aws.amazon.com/ec2/capacityblocks/pricing/
S9
AWS — accelerated instance specifications
aws.amazon.com/ec2/instance-types/accelerated-computing/
S10
Tenstorrent — vLLM TT plugin
github.com/tenstorrent/vllm-tt-plugin
S11
NVIDIA Dynamo — disaggregated serving
docs.nvidia.com/dynamo/components/router/disaggregated-serving
S12
Leviathan et al. — speculative decoding, ICML 2023
proceedings.mlr.press/v202/leviathan23a.html
S13
Supermicro — Data Center Building Block Solutions
www.supermicro.com/en/solutions/dcbbs
S14
Kubernetes — device plugins
kubernetes.io/docs/concepts/extend-kubernetes/compute-storage-net/device-plugins/
S15
vLLM — parallelism and scaling
docs.vllm.ai/en/latest/serving/parallelism_scaling/
Notes: Price provenance: AWS Capacity Blocks use an upfront reservation fee and dynamic rates; not On-Demand. Lambda prices are per GPU-hour and configurations differ. Support/taxes/egress and negotiated rates must be added or reconciled. Public framework sources are cited to establish available design mechanisms only. The native ATMOS backend, GPU-to-ATMOS KV format, speculative verification and heterogeneous pipeline remain proposed work. Kubernetes labels/discovery are only orchestration. OEM reference indicates available engineering services, not an executed partnership. EVIDENCE / ASSUMPTIONS Checked 1 October 2026. Published source facts, internal targets, and proposed numerical assumptions are not interchangeable. [S7] Lambda — public instance price list https://lambda.ai/pricing Snapshot 1 October 2026: 4x H100 SXM = $4.09/GPU-hour ($16.36/group-hour), 80GB/GPU; 900GiB host RAM. Single GH200 $2.29/hour (96GB). Single A10 $1.29/hour (24GB). 8x B200 $6.69/GPU-hour. Taxes extra; availability and negotiated pricing differ. [S8] AWS EC2 Capacity Blocks — public pricing https://aws.amazon.com/ec2/capacityblocks/pricing/ Snapshot 1 October 2026: p5.48xlarge N. Virginia $41.528/instance-hour (8 H100); p5.4xlarge $5.191. These are Capacity Block reservation rates, NOT On-Demand. AWS announces P5 $5.970/accelerator-hour effective 7 October 2026. Static annualization is not a three-year quote. [S9] AWS — accelerated instance specifications https://aws.amazon.com/ec2/instance-types/accelerated-computing/ P5.48xlarge: 8 H100, 640GB HBM3, 192 vCPU, 2TiB host memory, up to 3200Gbps EFAv2. P5.4xlarge: one H100, 80GB, 16vCPU, 256GiB; GPU Direct RDMA not supported on p5.4xlarge. [S10] Tenstorrent — vLLM TT plugin https://github.com/tenstorrent/vllm-tt-plugin Public precedent for a platform plugin containing model loading, worker execution and scheduling. It does not establish full native ATMOS model support. Pin exact releases and qualify the specific ATMOS target. [S11] NVIDIA Dynamo — disaggregated serving https://docs.nvidia.com/dynamo/components/router/disaggregated-serving Independent prefill/decode pools and KV handoff. Does not itself supply an ATMOS decoder or arbitrary cross-accelerator KV compatibility. [S12] Leviathan et al. — speculative decoding, ICML 2023 https://proceedings.mlr.press/v202/leviathan23a.html Draft-and-target verification algorithm. Distribution preservation requires the correct acceptance/correction procedure. No ATMOS speedup is supplied by this paper. [S13] Supermicro — Data Center Building Block Solutions https://www.supermicro.com/en/solutions/dcbbs Public modular infrastructure/OEM-integration capability; a reason for engagement, not a partnership or an ATMOS design commitment. [S14] Kubernetes — device plugins https://kubernetes.io/docs/concepts/extend-kubernetes/compute-storage-net/device-plugins/ Device discovery/resource advertisement and allocation. Pod labels are not hardware allocation or proof that a complete model is ready. [S15] vLLM — parallelism and scaling https://docs.vllm.ai/en/latest/serving/parallelism_scaling/ Public layer/pipeline parallelism precedent; not a ready-made heterogeneous GPU/ATMOS implementation.