## Slide 1
SANDISK / ATMOS
ENTERPRISE OFFERINGS / DECISION PROPOSAL
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
01
Three proposed offerings. E3.S-based appliance portfolio; not AWS EC2 or a shipping product catalog.
Three offerings.
One ATMOS platform.
What we deliver, how it works,
and why an enterprise would adopt it.
A
B
C
A NATIVE SERVICE
Independent MoE capacity
B PREFILL / DECODE
GPU prompts; ATMOS generation
C SPECULATIVE
Small drafter; large target verifier
Recommend A first. Qualify B and C only when their specific benefit is measured.
Notes: Open with the product distinction: these are three enterprise service offerings, not three ways to patch a GPU expert layer. A is an independent native MoE service. B separates complete GPU prefill from complete ATMOS decode. C pairs a small GPU drafter with an ATMOS target verifier. Recommend A as the base product because its customer integration is at the request boundary. B and C are conditional capabilities, not established ATMOS features. The removed whole-layer pipeline is not part of this portfolio. Use slides 1–14 for the decision discussion and slides 15–18 as backup. All appliance specifications, native runtime support and performance claims still require qualification.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.

## Slide 2
SANDISK / ATMOS
ENTERPRISE DEMAND
A banking example—and a bounded entry point.
Public adoption proves the workflow exists. It does not prove ATMOS performance or savings.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
02
[S1] Lloyds Banking Group, 29 Jan 2026. Pilot quantities and service limits are proposed inputs, not Lloyds disclosures.
PUBLISHED: LLOYDS / ATHENA
20,000
colleagues using the knowledge assistant
66%
reported average search-time reduction
What is not public
GPU inventory, token traffic, serving cost and the underlying MoE model.
PROPOSED ATMOS PILOT — NOT A CLAIMED LLOYDS DEPLOYMENT
Documents
Approved summaries / extraction
Eligibility policy
Model + context + deadline
ATMOS service
Complete native MoE request
Business review
Human accountability retained
FIRST SERVICE PROFILE
4,096 input / ≤512 output tokens • 8K total cap • proposed p95 completion ≤120 s
Notes: Lloyds is the public enterprise-demand example, not a claimed ATMOS customer. The public release reports Athena used by 20,000 colleagues and a 66% reduction in average search time. It does not disclose the model, GPU inventory, token traffic or inference cost. The document-processing flow is a proposed pilot inspired by that deployment pattern. The pilot retains the source deck's 4,096-input-token / up-to-512-output-token profile, an 8K total-context cap and proposed p95 completion within 120 seconds. The deadline includes queueing, prefill and decode. Do not present it as a measured ATMOS SLA. Retrieval, document authorization and autonomous banking decisions remain outside the initial model-serving product.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S1] Lloyds Banking Group — AI-driven benefits, 29 Jan 2026
https://www.lloydsbankinggroup.com/media/press-releases/2026/lloyds-banking-group/ai-driven-benefits-2026.html
Athena used by 20,000 colleagues; reported average search-time reduction 66%. Not an ATMOS customer, disclosed GPU deployment, token trace or inference-cost comparison.

## Slide 3
SANDISK / ATMOS
PORTFOLIO
Three offerings solve three different constraints.
Each is a complete customer offer—not a feature hidden inside an existing GPU expert layer.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
03
Proposed product definitions, expanded from source deck A/B/C. Full native ATMOS model support is a common delivery gate.
A
ATMOS-native
MoE appliance
CUSTOMER PROBLEM
Need more private inference capacity without altering the GPU engine.
WHAT SANDISK OFFERS
An independent endpoint: complete prefill + decode on ATMOS.
Eligible requests leave the GPU queue; service groups scale independently.
LEAD • request boundary
B
GPU prefill →
ATMOS decode
CUSTOMER PROBLEM
Need fast prompt processing, but output generation occupies the GPU pool.
WHAT SANDISK OFFERS
A paired service: complete GPU prefill + native ATMOS decoder + KV bridge.
GPU prefill and ATMOS decode can be sized separately.
CONDITIONAL • KV boundary
C
Speculative
inference node
CUSTOMER PROBLEM
Native target decoding spends too much time per committed token.
WHAT SANDISK OFFERS
A small GPU draft model + ATMOS target MoE + verification scheduler.
Several target-approved tokens may be produced per target cycle.
RESEARCH • token-block boundary
Notes: Explain each offering in the same order: customer problem, what we deliver, execution boundary and benefit to prove. A sells independent inference capacity. B sells a coordinated two-phase service with a real cache handoff. C sells target-model acceleration through verified draft proposals. The native ATMOS runtime is shared, but the integration contracts are different. A needs endpoint registration and routing policy. B needs access to a compatible GPU prefill connector. C needs a new draft/target runtime and state protocol. None follows from simply applying labels to a Pod. Do not promise a universal throughput uplift or lower cost before testing the intended workload.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.

## Slide 4
SANDISK / ATMOS
A / EXECUTION ARCHITECTURE
A | A complete model service, separate from GPUs.
The customer sends each request to one eligible endpoint. ATMOS is not a GPU weight cache.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
04
[S5] Native-platform plugin precedent. [S10] Device allocation. ATMOS implementation and memory/fabric behavior remain proposed.
Customer gateway / job policy
Choose by approved model, context, queue and deadline
EXISTING SERVICE
NEW ATMOS-NATIVE SERVICE GROUP
NVIDIA / AMD GPU pool
Existing runtime + model
Prefill, decode and GPU KV
Interactive / unqualified requests
Native runtime: prefill + decode
Attention → router → experts → combine → output
HBF: full-model weights
LPDDR/SRAM: active KV + work
One complete serving group may span several E3.S devices.
DATA AT THE BOUNDARY
Requests and responses only. No GPU KV handoff or per-layer hidden-state exchange.
Notes: Follow one request. The gateway chooses one eligible complete service, not both. On the ATMOS side, the native runtime performs full prompt processing, creates its own active KV and then runs complete decode, including attention, routing, experts, combine and output. GPU-served requests retain their independent GPU cache. No GPU KV or per-layer target activation is sent to ATMOS for offering A. HBF is the proposed full-model weight store; NPU-addressable working memory must hold active KV and scratch. A large model may span several modules, in which case its native inter-device communication must be qualified. The public TT plugin is a packaging precedent, not an ATMOS compatibility certificate. A separate appliance protects the existing GPU deployment; a shared Kubernetes deployment still needs approved host and cluster changes.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S5] Tenstorrent — vLLM platform plugin
https://github.com/tenstorrent/vllm-tt-plugin
Public precedent for a native platform plugin with loading, worker execution and scheduling. Does not certify ATMOS silicon, HBF/LPDDR access, full-model support or service rates.
[S10] Kubernetes — device plugins
https://kubernetes.io/docs/concepts/extend-kubernetes/compute-storage-net/device-plugins/
Resource discovery/advertisement and allocation. Labels do not allocate NPUs or establish model readiness. Proposed Sandisk whole-device allocation and lifecycle are new product work.
[I1] Internal ATMOS planning envelope
Source deck slides 5–6 and 12; supplied ATMOS proposal. Up to 128 GB HBF per E3.S, 100 GB application study budget, 8–16 GB LPDDR, 200 GB/s local-read target. Unqualified device targets: not production specification, native runtime support, price or throughput.

## Slide 5
SANDISK / ATMOS
A / CUSTOMER OFFER AND VALUE
A | Move eligible requests off the GPU service.
A private inference endpoint with an explicit model, context, deadline and support contract.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
05
All traffic quantities below are retained source-deck pilot assumptions. No measured capacity, node reduction or SLA is implied.
THE CUSTOMER RECEIVES
Qualified appliance
CPU host, ATMOS modules, working memory and tested fabric.
Supported model service
Native runtime, versioned full-model pack and API contract.
Operations package
Admission, readiness, tenant isolation, updates and recovery.
ILLUSTRATIVE DEMAND ALLOCATION
48,000
model calls/day before the proposed split
28,800
calls/day retained on GPU service
19,200
eligible jobs/day assigned to ATMOS
40% of calls redirected ≠ 40% fewer GPUs.
Savings require an actual reduction in required GPU capacity.
BENEFIT TO PROVE
Protect interactive capacity; add a separate private job pool at lower cost per accepted job.
Notes: The demand split is an illustration inherited from the source deck: 20,000 users × 40% daily activity × 6 calls gives 48,000 calls/day. A proposed 40% eligible share directs 19,200 jobs to ATMOS and leaves 28,800 calls on the GPU service. These are not Lloyds measurements. Under the original eight-hour service window and 3× peak assumption, ATMOS-eligible peak demand is 2 requests/s. Redirecting 40% of calls does not imply 40% less GPU capacity because request sizes, service time, utilization and reserve differ. The customer benefit is independently managed private capacity and reduced competition with interactive work. Savings are credited only when capacity is retired, usefully repurposed or not purchased. Compare ATMOS with a GPU allowed the same model, deadline and batching policy.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S1] Lloyds Banking Group — AI-driven benefits, 29 Jan 2026
https://www.lloydsbankinggroup.com/media/press-releases/2026/lloyds-banking-group/ai-driven-benefits-2026.html
Athena used by 20,000 colleagues; reported average search-time reduction 66%. Not an ATMOS customer, disclosed GPU deployment, token trace or inference-cost comparison.
[S10] Kubernetes — device plugins
https://kubernetes.io/docs/concepts/extend-kubernetes/compute-storage-net/device-plugins/
Resource discovery/advertisement and allocation. Labels do not allocate NPUs or establish model readiness. Proposed Sandisk whole-device allocation and lifecycle are new product work.

## Slide 6
SANDISK / ATMOS
B / EXECUTION ARCHITECTURE
B | GPU prefill feeds an ATMOS-native decoder.
Split once at the serving-phase boundary—not repeatedly at each MoE expert layer.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
06
[S6–S8] Disaggregated-serving / cache-transport precedents. A GPU–ATMOS KV bridge and native decoder are new qualification work.
One coordinated service endpoint
Admit a request only when both phases can meet its service contract
GPU PREFILL GROUP
Complete prompt computation
Full compatible model weights
Attention + experts on GPU
Prompt KV created in GPU memory
ATMOS DECODE GROUP
Complete token generation
Same target model weights in HBF
Imported active KV in working memory
Attention + experts + next-token loop
KV blocks +
continuation state
Qualified copy /
layout conversion
AFTER HANDOFF
GPU prefill accepts other prompts. ATMOS finishes decode without a per-layer GPU return.
Notes: GPU prefill runs the complete target model, including attention and FFNs. It therefore retains full compatible model weights. ATMOS also holds the target weights and implements the complete decoder. At the phase boundary, transfer KV blocks and continuation metadata. This may use blockwise or layerwise transfers; it does not mean one DMA command. The contract must define model identity, positions, dtype/scales, cache layout, head/shard ownership, fences and first-token handling. After a successful handoff, the prefill pool can accept other work. If the decoder backs up, that benefit is not guaranteed. Native ATMOS decode has no repeated return to the GPU at each model layer. Public Dynamo, vLLM and LMCache mechanisms do not supply a qualified ATMOS decoder or guarantee compatible cache formats.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S6] NVIDIA Dynamo — disaggregated serving
https://docs.nvidia.com/dynamo/components/router/disaggregated-serving
Separate prefill/decode worker pools and KV handoff are documented. A cross-GPU/ATMOS deployment, its backend and cache interoperability must be implemented and qualified separately.
[S7] vLLM — disaggregated prefilling
https://docs.vllm.ai/en/latest/features/disagg_prefill/
Connector-based KV handoff; an ordinary chat API does not expose native cache state. Public framework capability does not imply an ATMOS decoder exists.
[S8] LMCache — KV management layer
https://docs.lmcache.ai/
Public KV-management and transfer framework. It is not an attention kernel, full ATMOS model runtime or proof of a compatible device layout.
[S2] Qwen3-235B-A22B — model configuration
https://huggingface.co/Qwen/Qwen3-235B-A22B/blob/main/config.json
94 layers, 4 KV heads, head dimension 128, 128 experts, top-8. KV calculations assume BF16 values and full logical cached context; exclude duplication, block rounding and workspace.

## Slide 7
SANDISK / ATMOS
B / CUSTOMER OFFER AND VALUE
B | Share fast prefill; scale output capacity separately.
Useful when prompt processing benefits from GPU compute and a qualified ATMOS decoder is competitive.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
07
Calculated Qwen3-235B BF16 logical KV from [S2]. Workload is a proposed study profile; no target latency is predicted.
What we sell
A qualified paired service: GPU prefill configuration + ATMOS decode appliance + KV bridge + joint admission and lifecycle.
Why the customer cares
Keep GPU capacity focused on prompt processing. Add decode groups without buying a complete GPU serving replica for every group.
THE HANDOFF IS REAL WORK
0.73 GiB
logical KV per 4,096-token prompt
1.47 GiB/s
at the proposed 2-request/s handoff rate
Before layout duplication, staging, protocol and burst headroom.
Size GPU:ATMOS counts from measured prefill/decode rates.
CUSTOMER CHANGE
GPU KV-export connector is required. A chat endpoint alone cannot enable this offering.
Notes: This is a purpose-built paired service. It can use a newly provisioned GPU prefill pool rather than alter the customer's protected GPU service, but that new pool still needs connector integration. GPU and ATMOS group counts are determined by measured rates, input/output distributions and reserve policy. Do not prescribe an unmeasured 1:4 or 1:8 ratio. Qwen3-235B BF16 logical prompt KV is 2 × 94 × 4 × 128 × 2 × 4,096 = 788,529,152 bytes, or 0.734375 GiB. At 2 requests/s this is 1.46875 GiB/s, before layout duplication, staging and protocol costs. No prefix-reuse or compression benefit is assumed. TTFT includes the exposed prefill/handoff cost; ATMOS decode must separately meet TPOT. Full model weights are present in both phase pools, so do not inherit the old GPU weight-reclamation claim.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S2] Qwen3-235B-A22B — model configuration
https://huggingface.co/Qwen/Qwen3-235B-A22B/blob/main/config.json
94 layers, 4 KV heads, head dimension 128, 128 experts, top-8. KV calculations assume BF16 values and full logical cached context; exclude duplication, block rounding and workspace.
[S6] NVIDIA Dynamo — disaggregated serving
https://docs.nvidia.com/dynamo/components/router/disaggregated-serving
Separate prefill/decode worker pools and KV handoff are documented. A cross-GPU/ATMOS deployment, its backend and cache interoperability must be implemented and qualified separately.
[S7] vLLM — disaggregated prefilling
https://docs.vllm.ai/en/latest/features/disagg_prefill/
Connector-based KV handoff; an ordinary chat API does not expose native cache state. Public framework capability does not imply an ATMOS decoder exists.
[S8] LMCache — KV management layer
https://docs.lmcache.ai/
Public KV-management and transfer framework. It is not an attention kernel, full ATMOS model runtime or proof of a compatible device layout.

## Slide 8
SANDISK / ATMOS
C / EXECUTION ARCHITECTURE
C | Small GPU drafts; ATMOS verifies the target.
The large MoE stays on ATMOS. The GPU proposes tokens—it does not execute target-model layers.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
08
[S9] Speculative-decoding algorithm. The cross-device implementation, acceptance rate and speedup are proposed—not measured.
Speculative serving scheduler
One user request • two models • one target-approved response
SMALL DRAFT MODEL / GPU
Propose a token block
Draft weights + its own KV
Small supported GPU configuration
Candidate block length is tunable
LARGE TARGET MOE / ATMOS
Score, accept or correct
Target weights + target KV
Attention and expert execution
Reclaim rejected speculative state
Candidate tokens +
verification metadata
Committed prefix /
correction to drafter
STATE OWNERSHIP
Draft and target KV are separate. No transfer of the draft KV into the ATMOS target.
Notes: The drafter is a separate small model selected for speed, tokenizer compatibility and acceptance. The ATMOS target remains the approved large MoE. Each has its own KV cache, and each must initialize prompt state. This offering does not silently include GPU prefill of the target from offering B. Candidate tokens plus algorithm-required metadata are exchanged per verification cycle. Some exact protocols require draft probability information, so token IDs alone are not a universal wire contract. The target scores candidates, commits accepted output and applies the prescribed correction procedure. Rejected speculative cache state is safely reclaimed, and the draft follows the committed prefix. This is not voting or a quality-classifier shortcut. Distribution preservation is an algorithmic property under the specified procedure; the implementation still needs numerical and end-to-end validation.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S9] Leviathan et al. — Fast Inference from Transformers via Speculative Decoding
https://proceedings.mlr.press/v202/leviathan23a.html
ICML 2023 algorithmic precedent for draft proposals and target acceptance/correction. Distribution preservation requires the correct algorithm, not voting or a quality classifier. No ATMOS timing or acceptance rate is supplied.
[S5] Tenstorrent — vLLM platform plugin
https://github.com/tenstorrent/vllm-tt-plugin
Public precedent for a native platform plugin with loading, worker execution and scheduling. Does not certify ATMOS silicon, HBF/LPDDR access, full-model support or service rates.

## Slide 9
SANDISK / ATMOS
C / CUSTOMER OFFER AND VALUE
C | More committed tokens per target cycle is the prize.
A small draft GPU is worthwhile only when accepted target output pays for drafting and verification.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
09
New arithmetic illustration, not an ATMOS benchmark or predicted gain. [S9] supplies the algorithm—not these timings.
ILLUSTRATIVE CYCLE — 4 CANDIDATES
Case
Time / cycle
Committed
Effective
Native target
80 ms
1 token
80 ms/token
Useful speculation
120 ms
3 tokens
40 ms/token
Low acceptance
120 ms
1 token
120 ms/token
2× in the useful example; slower when acceptance is poor.
What we sell
A qualified draft/target pair, block-verification scheduler, target-correct sampling, cache rollback and per-workload tuning.
Customer benefit to earn
Faster long answers or more accepted output from the same ATMOS target group—without replacing its approved target model.
ADOPTION GATE
Measure accepted tokens/s and latency after draft cost. Disable speculation when it loses.
Notes: All timings on this slide are new illustrative inputs. The ordinary target is assumed to take 80 ms per token. A speculative cycle, including drafting, target verification and protocol, is assumed to take 120 ms. If that cycle commits three output tokens on average, it takes 40 ms per committed token, or twice the ordinary rate. If only one token is committed, it is slower at 120 ms/token. Four candidate tokens is not the same as three committed tokens. Define accepted output consistently, including any corrected or bonus token produced by the chosen algorithm. Real verification can touch more experts and consume more cache or bandwidth, so block execution does not guarantee a gain. Qualify the complete draft/target pair and retain normal target decoding when speculation loses.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S9] Leviathan et al. — Fast Inference from Transformers via Speculative Decoding
https://proceedings.mlr.press/v202/leviathan23a.html
ICML 2023 algorithmic precedent for draft proposals and target acceptance/correction. Distribution preservation requires the correct algorithm, not voting or a quality classifier. No ATMOS timing or acceptance rate is supplied.

## Slide 10
SANDISK / ATMOS
COMMON APPLIANCE PLATFORM
One ATMOS-first node—with optional GPU roles.
Reference engineering study, not a validated BOM. Device-group size follows model and service needs.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
10
[S4] EPYC CPU facts. [I1] Internal ATMOS targets. Host population, topology and working-memory reserve are proposed.
HOST / CONTROL PLANE
EPYC 9355P reference: 32 cores
128 PCIe Gen5 lanes • 12 DDR5 channels
Proposed: 384 GB DDR5
2 × 3.84 TB mirrored NVMe
Dual 100 GbE • BMC • redundant power
ATMOS EXECUTION PLANE — 8-DEVICE STUDY
A0
A1
A2
A3
A4
A5
A6
A7
1,024 GB nominal HBF / 800 GB study budget
128 GB LPDDR at the 16 GB/module target
96 GB after a provisional 4 GB/device reserve
2 × (Gen5 x16 → 4 × Gen5 x4) study branches.
Native device fabric and per-device KV fit remain open gates.
A No GPU required
B Qualified GPU prefill pool
C Small GPU drafter
Notes: This is the source deck's OEM study configuration, not a validated BOM. The EPYC 9355P is a public CPU reference. Host DDR5, mirrored NVMe, dual 100 GbE and chassis details are proposed selections. Host DRAM is not automatically NPU-addressable active KV memory. Eight modules give 1,024 GB nominal HBF; the study allocates 100 GB per device, or 800 GB. Select the 16 GB LPDDR target for this study; a provisional 4 GB/device reserve leaves 96 GB aggregate, not a unified pool. Two four-device branches with x16 uplinks consume 32 host lanes, so they do not save lanes relative to eight direct x4 links. Native inter-device collectives and failure domains require validation. B's prefill pool may be a separate supported GPU node. C's draft GPU is selected only after model fit and acceptance testing.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S4] AMD — EPYC 9355P specification
https://www.amd.com/en/products/processors/server/epyc/9005-series/amd-epyc-9355p.html
Public CPU reference: 32 cores, one socket, 128 PCIe Gen5 lanes and 12 DDR5 channels. All appliance population, cooling and network selections are proposed OEM study inputs, not certification.
[I1] Internal ATMOS planning envelope
Source deck slides 5–6 and 12; supplied ATMOS proposal. Up to 128 GB HBF per E3.S, 100 GB application study budget, 8–16 GB LPDDR, 200 GB/s local-read target. Unqualified device targets: not production specification, native runtime support, price or throughput.

## Slide 11
SANDISK / ATMOS
CUSTOMER INTEGRATION / PRODUCT OBLIGATIONS
A integrates at the API. B and C require runtime integration.
One common native ATMOS stack; B and C add different runtime contracts—not just gateway rules.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
11
[S5–S10] Public mechanisms; ATMOS-specific backends, connectors, verification and release support are proposed deliverables.
Boundary
A Native service
B Prefill → decode
C Speculative
Customer integration
Endpoint + policy; separate appliance or dedicated K8s nodes.
GPU prefill connector + paired-service configuration.
Paired draft/target runtime + speculative scheduler.
New ATMOS work
Full prefill/decode, attention, KV, experts and sampling path.
Full decoder + KV import/conversion + continuation.
Full target + block verification + safe KV rollback.
GPU role / state
No GPU needed for assigned request. GPU service retains its own KV.
Full-model prefill; exports target KV. Weights also reside on ATMOS.
Small draft model with separate KV; no target-KV export.
Enterprise operation
Allocation, readiness, admission, tenant isolation, telemetry, update and recovery.
Same common package + handoff ownership, cancellation and failure recovery.
Same common package + model-pair lifecycle and verification telemetry.
OWNERS: SanDisk — service/release | Tenstorrent — native backend | OEM — hardware/fabric/lifecycle
Notes: Separate customer impact from vendor firmware changes. A uses an additional endpoint and does not need changes to the existing GPU inference engine. B requires a compatible GPU prefill export interface. C requires draft/target serving integration. B or C may be delivered as new services alongside the untouched customer deployment. None is merely a gateway rule. The design prohibits private NVIDIA or AMD driver/firmware patches, but does not assume every public interface works on every platform. Kubernetes allocates hardware resources; the ATMOS runtime executes the model; readiness must represent complete model coverage. SanDisk owns service qualification and lifecycle, Tenstorrent supplies the committed native backend, and the OEM owns the supported physical configuration. Those assignments still need explicit partner commitments.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S5] Tenstorrent — vLLM platform plugin
https://github.com/tenstorrent/vllm-tt-plugin
Public precedent for a native platform plugin with loading, worker execution and scheduling. Does not certify ATMOS silicon, HBF/LPDDR access, full-model support or service rates.
[S6] NVIDIA Dynamo — disaggregated serving
https://docs.nvidia.com/dynamo/components/router/disaggregated-serving
Separate prefill/decode worker pools and KV handoff are documented. A cross-GPU/ATMOS deployment, its backend and cache interoperability must be implemented and qualified separately.
[S7] vLLM — disaggregated prefilling
https://docs.vllm.ai/en/latest/features/disagg_prefill/
Connector-based KV handoff; an ordinary chat API does not expose native cache state. Public framework capability does not imply an ATMOS decoder exists.
[S8] LMCache — KV management layer
https://docs.lmcache.ai/
Public KV-management and transfer framework. It is not an attention kernel, full ATMOS model runtime or proof of a compatible device layout.
[S9] Leviathan et al. — Fast Inference from Transformers via Speculative Decoding
https://proceedings.mlr.press/v202/leviathan23a.html
ICML 2023 algorithmic precedent for draft proposals and target acceptance/correction. Distribution preservation requires the correct algorithm, not voting or a quality classifier. No ATMOS timing or acceptance rate is supplied.
[S10] Kubernetes — device plugins
https://kubernetes.io/docs/concepts/extend-kubernetes/compute-storage-net/device-plugins/
Resource discovery/advertisement and allocation. Labels do not allocate NPUs or establish model readiness. Proposed Sandisk whole-device allocation and lifecycle are new product work.

## Slide 12
SANDISK / ATMOS
TECHNICAL SCOPE / SERVICE ENVELOPE
Working memory sets the usable service envelope.
Weight residency is only one test. Every offering also needs native attention, KV and a qualified device fabric.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
12
[S2–S3, S11] Model geometry; [I1] internal 100 GB/device HBF study budget. Raw-byte floors are not supported device counts.
Model / study role
Full weights: FP8 / 16-bit
100-GB HBF raw floor
Qwen3-30B-A3B • bring-up
30.5 / 61 GB
1 / 1 modules
Qwen3-235B-A22B • primary study
235 / 470 GB
3 / 5 modules
DeepSeek-V3 • later expansion
671 / 1,342 GB
7 / 14 modules
QWEN 235B: SAME MODEL, DIFFERENT ACTIVE-STATE REQUIREMENT
47 GiB
32 sequences × 8K total context; BF16 KV
188 GiB
32 sequences × 32K: exceeds 128 GB nominal LPDDR
Notes: Account for full model weights rather than only experts. The raw FP8/16-bit numbers and 100 GB/device capacity floors are inherited from the source deck. They exclude scales, mixed-precision tensors, alignment, replicas and runtime memory. A raw capacity floor is not a recommendation for device count or a statement of compiler support. Qwen3-235B with BF16 KV needs 1.46875 GiB per 8K sequence; 32 sequences need 47 GiB. At 32K total context, the same 32 sequences need 188 GiB, which exceeds eight 16 GB LPDDR devices before reserve. Per-device sharding, layout replication and scratch can tighten the budget further. DeepSeek's MLA needs its own cache calculation; do not apply the Qwen GQA formula. Different models also require separate quality acceptance.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S2] Qwen3-235B-A22B — model configuration
https://huggingface.co/Qwen/Qwen3-235B-A22B/blob/main/config.json
94 layers, 4 KV heads, head dimension 128, 128 experts, top-8. KV calculations assume BF16 values and full logical cached context; exclude duplication, block rounding and workspace.
[S3] Qwen3-30B-A3B — model configuration
https://huggingface.co/Qwen/Qwen3-30B-A3B/blob/main/config.json
48 layers, 4 KV heads, head dimension 128; 128 experts and top-8. Source deck/publisher model card: about 30.5B total and 3.3B active parameters.
[S11] DeepSeek-V3 — model configuration
https://huggingface.co/deepseek-ai/DeepSeek-V3/blob/main/config.json
Source deck retains publisher model geometry: approximately 671B total, 37B active, 256 routed plus shared expert, 58 MoE and 3 dense layers. MLA cache must be sized separately; Qwen GQA formula does not apply.
[I1] Internal ATMOS planning envelope
Source deck slides 5–6 and 12; supplied ATMOS proposal. Up to 128 GB HBF per E3.S, 100 GB application study budget, 8–16 GB LPDDR, 200 GB/s local-read target. Unqualified device targets: not production specification, native runtime support, price or throughput.

## Slide 13
SANDISK / ATMOS
SELECTION / CUSTOMER VALUE
Lead with A. Add B or C for a measured bottleneck.
Success means more useful completed work under the same quality and service contract—not simply more memory.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
13
Proposed prioritization. Each option is tested against an optimized same-workload control, including GPU batch serving.
Offer
Best customer situation
Benefit to demonstrate
Go / no-go evidence
A Native appliance
Private document jobs with an approved completion deadline.
Separate eligible work from GPU demand; independently managed capacity.
Native full-model quality, jobs/hour, completion deadline and operational cost.
B Prefill / decode
Native ATMOS decode is useful, but prompt processing is limiting.
Share prompt-processing GPUs; independently expand generation capacity.
Combined TTFT/TPOT improves the service after KV transfer and duplicated models.
C Speculative node
Target decoding is limiting and draft acceptance is high.
More target-approved output or faster long answers from the same target group.
Accepted tokens/s and latency win after drafting, rollback and protocol overhead.
THE CUSTOMER PROMISE
A named model service with a known envelope, clear ownership and a reproducible benefit.
Notes: Choose by the bottleneck, not by architectural novelty. A is the initial candidate for private document jobs where a native service meets the quality and deadline requirement. B is useful only if ATMOS decode is competitive and prompt processing is the remaining issue. C is useful only if target verification plus drafting produces more accepted output or lower latency. Each option must beat a same-workload control with matching precision, context, availability and operating hours. Reduced GPU utilization alone is not a saving. Pricing and power are measured or quoted later. Do not qualify B or C merely because A works; cache interoperability and speculative correctness are independent obligations.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.

## Slide 14
SANDISK / ATMOS
DELIVERY PLAN / DECISION
Four gates turn the portfolio into a supported product.
Build the native platform once. B and C are specific capability gates on top—not separate full stacks.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
14
Simulator/emulator work can overlap. Surrogate timing is not measured ATMOS performance. Candidate owners are not partner commitments.
1 SIMULATOR
Size the full native model
Attention/KV + HBF/NPU
Device-fabric contention
Required service envelope
PRE-SILICON
2 EMULATOR
Operate the real interfaces
Complete request/response
Pack, queue, failure contracts
Correct reference execution
PRE-SILICON
3 PHYSICAL NODE
Prove native A first
Actual quality + latency
Working-memory/fabric fit
Then test B handoff / C verify
SILICON GATE
4 CUSTOMER PILOT
Demonstrate useful work
Approved bank job trace
Failover, update and recovery
Measured business benefit
RELEASE GATE
APPROVE NOW
One model/workload • a TT native-runtime scope • an OEM memory/fabric study • one pilot owner
Notes: There are three offerings and four evidence gates. The simulator covers the complete native model, including attention, active KV and the device fabric. The emulator operates real software contracts and returns correct model results on surrogate compute, without claiming ATMOS silicon performance. Physical testing proves native offering A first and then exercises B's KV handoff and C's verification/rollback where justified. The customer pilot uses an authorized job trace and includes failure, upgrade, rollback and operating-cost evidence. Simulator and emulator work can overlap. Ask for one native runtime commitment, one OEM memory/fabric study and one named pilot owner. These gates do not imply a guaranteed six-month runtime delivery or product date.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.

## Slide 15
SANDISK / ATMOS
BACKUP / INTERFACE CONTRACTS
Three contracts—not one generic “ATMOS adapter.”
The integration boundary determines engineering work and what may cross it.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
15
Expanded engineering detail derived from A/B/C boundaries. [S5–S10] provide framework/algorithm precedents only.
Contract
What crosses
What we must implement / verify
A Request API
Prompt / token input, model/version, generation limits, tenant identity; response or job result.
Tokenizer and API parity; model readiness; queue/deadline admission; isolation; cancellation and complete-group failure behavior.
B KV handoff
Target KV blocks, model hash, positions, head/shard map, dtype/scales, block layout, transfer fences and continuation state.
Correct KV conversion/import; ownership transfer; first-token contract; stale/reset handling; no duplicated/missing state; measured handoff.
C Verification cycle
Draft candidates + required probability / protocol metadata; committed tokens and corrections back.
Correct target scoring/masks; acceptance/correction; speculative KV commit/rollback; tokenizer alignment; drafter resynchronization.
COMMON BACKEND
Full-model compiler/loader + attention/KV + MoE runtime + device fabric; not an FFN-only pack.
Notes: Use this slide when asked what the actual adapter contains. A is a service API contract. B is a state-transfer contract. C is a verification-cycle contract. They are not interchangeable. B needs exact model/cache identities, positions, shard mapping and safe ownership; a pointer or a byte copy alone is insufficient. C needs the sampling protocol's required metadata and rejected-state cleanup, not just a list of guesses. All offerings rely on a full native ATMOS model backend, including attention, router, experts, combine and output. That is a broader deliverable than the earlier ExpertPack-only FFN compiler. Host-side control or sampling is acceptable only when declared, supported and included in the service cost.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S5] Tenstorrent — vLLM platform plugin
https://github.com/tenstorrent/vllm-tt-plugin
Public precedent for a native platform plugin with loading, worker execution and scheduling. Does not certify ATMOS silicon, HBF/LPDDR access, full-model support or service rates.
[S6] NVIDIA Dynamo — disaggregated serving
https://docs.nvidia.com/dynamo/components/router/disaggregated-serving
Separate prefill/decode worker pools and KV handoff are documented. A cross-GPU/ATMOS deployment, its backend and cache interoperability must be implemented and qualified separately.
[S7] vLLM — disaggregated prefilling
https://docs.vllm.ai/en/latest/features/disagg_prefill/
Connector-based KV handoff; an ordinary chat API does not expose native cache state. Public framework capability does not imply an ATMOS decoder exists.
[S8] LMCache — KV management layer
https://docs.lmcache.ai/
Public KV-management and transfer framework. It is not an attention kernel, full ATMOS model runtime or proof of a compatible device layout.
[S9] Leviathan et al. — Fast Inference from Transformers via Speculative Decoding
https://proceedings.mlr.press/v202/leviathan23a.html
ICML 2023 algorithmic precedent for draft proposals and target acceptance/correction. Distribution preservation requires the correct algorithm, not voting or a quality classifier. No ATMOS timing or acceptance rate is supplied.
[S10] Kubernetes — device plugins
https://kubernetes.io/docs/concepts/extend-kubernetes/compute-storage-net/device-plugins/
Resource discovery/advertisement and allocation. Labels do not allocate NPUs or establish model readiness. Proposed Sandisk whole-device allocation and lifecycle are new product work.

## Slide 16
SANDISK / ATMOS
BACKUP / MEMORY ARITHMETIC
Size prompt transfer and active state separately.
Qwen GQA example: FP8 model weights do not imply FP8 KV. The table assumes BF16 KV throughout.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
16
Calculated from [S2–S3]. Logical bytes only: add block rounding, replication, converter/staging buffers and native workspace.
KV bytes = 2 × layers × KV heads × head width × bytes/value × cached tokens
Model
4K prompt KV
8K total KV
32 × 8K
Qwen3-30B (48 layers)
0.375 GiB
0.750 GiB
24.0 GiB
Qwen3-235B (94 layers)
0.734 GiB
1.469 GiB
47.0 GiB
Offering B transfer
4K prompt: 0.734 GiB/request.
512 more tokens add ~94 MiB of KV.
2 RPS transfers 1.469 GiB/s logically.
Native working-memory limit
Eight ×16 GB =128 GB nominal LPDDR.
A 4 GB/device reserve leaves96 GB aggregate.
Per-device fit—not aggregate arithmetic—decides.
Notes: Unrounded Qwen235 values: each cached token uses 192,512 bytes of logical BF16 KV. A 4,096-token prefix uses 788,529,152 bytes (0.734375 GiB); 8,192 tokens use 1,577,058,304 bytes (1.46875 GiB); 512 generated tokens add 98,566,144 bytes (94 MiB). Two 4K-prefix handoffs per second therefore carry 1.46875 GiB/s logically. Qwen30 uses 98,304 bytes per cached token, producing 0.375 GiB at 4K and 0.75 GiB at 8K. Total context includes prompt and generated tokens. FP8 weights do not change these BF16 KV assumptions. The nominal 128 GB and remaining 96 GB LPDDR amounts are decimal GB. Working-memory fit and communication must be evaluated per device. Neither HBF spill nor external host/CXL memory is counted as free active KV capacity.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S2] Qwen3-235B-A22B — model configuration
https://huggingface.co/Qwen/Qwen3-235B-A22B/blob/main/config.json
94 layers, 4 KV heads, head dimension 128, 128 experts, top-8. KV calculations assume BF16 values and full logical cached context; exclude duplication, block rounding and workspace.
[S3] Qwen3-30B-A3B — model configuration
https://huggingface.co/Qwen/Qwen3-30B-A3B/blob/main/config.json
48 layers, 4 KV heads, head dimension 128; 128 experts and top-8. Source deck/publisher model card: about 30.5B total and 3.3B active parameters.
[I1] Internal ATMOS planning envelope
Source deck slides 5–6 and 12; supplied ATMOS proposal. Up to 128 GB HBF per E3.S, 100 GB application study budget, 8–16 GB LPDDR, 200 GB/s local-read target. Unqualified device targets: not production specification, native runtime support, price or throughput.

## Slide 17
SANDISK / ATMOS
BACKUP / COMMERCIAL VALIDATION
Keep one cost test—not a page of savings forecasts.
The customer buys accepted work. HBF capacity, low GPU utilization and nominal device counts are not savings.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
17
Retained source-deck design-to-cost assumptions only. No ATMOS quote, measured throughput or guaranteed TCO is available.
$80k
inherited appliance purchase allowance
~$141k
inherited three-year modeled node cost
Not a quote
Replace with OEM / SanDisk pricing
Compare: total delivered cost ÷ work completed within quality + deadline
A Cost boundary
Credit GPU capacity only if it is retired, repurposed with value or not purchased.
B Cost boundary
Include GPU prefill, duplicate weights, KV transfer and decode reserve.
C Cost boundary
Include draft GPU, rejected work and verification overhead.
Notes: The dollar figures are retained design-to-cost assumptions, not an updated quote. The source model is $80,000 capex + 3 × $12,000 support + 3 × $6,000 site/network/admin + 3 × (1.6 kW × 1.4 PUE × $0.12/kWh × 8,760 hours) = $141,064.064. The assumed 1.6 kW draw is not a hardware specification. Taxes, financing, product R&D and customer migration are not included in that node allowance. Published cloud price tables and large fleet savings forecasts have been removed from the main story. Formal comparisons require current quotes, real operating hours, measured rates and matched reserve capacity. Offering B adds GPU prefill and KV transfer cost; C adds draft compute and rejected work. A slower cheaper node can still produce a more expensive fleet.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.

## Slide 18
SANDISK / ATMOS
BACKUP / EVIDENCE REGISTER
Evidence behind the design—and what remains proposed.
Clickable public sources; detailed scope and assumptions are also in speaker notes.
INTERNAL PROPOSAL • 01 OCT 2026 • ATMOS RESULTS / PRODUCT SUPPORT NOT YET QUALIFIED
18
Source basis: supplied executive deck. Public technical references revisited 1 October 2026.
S1
Lloyds / Athena
Public adoption and search-time result.
S2
Qwen3-235B configuration
Layer/head geometry and cache arithmetic.
S3
Qwen3-30B configuration
Smaller-model geometry.
S4
AMD EPYC 9355P
CPU reference; not an ATMOS-certified node.
S5
Tenstorrent vLLM plugin
Native-runtime packaging precedent.
S6
Dynamo disaggregated serving
Prefill/decode orchestration precedent.
S7
vLLM disaggregated prefilling
Connector boundary and integration scope.
S8
LMCache
KV management / transport, not an NPU runtime.
S9
Speculative decoding / ICML 2023
Correct acceptance/correction algorithm.
S10
Kubernetes device plugins
Hardware resource advertisement and allocation.
PROPOSED: ATMOS-native support, service rates, GPU–ATMOS KV compatibility, speculative gains, OEM BOM and prices.
Notes: The supplied executive deck remains the basis. The revision retains the native, prefill/decode and speculative offerings, the OEM study envelope, model sizing and bounded bank pilot. It expands execution diagrams, deliverables and customer benefit explanations, while removing whole-layer pipelining and most financial detail. New timing and traffic examples are explicitly calculated or illustrative. Public framework sources establish available concepts and extension mechanisms only, not ATMOS certification. Private ATMOS specifications remain planning targets. All three customer benefits must be demonstrated on a named model, service envelope and physical configuration before a product claim.
SOURCES / ASSUMPTIONS
Published facts, internal targets, illustrative arithmetic and proposed implementation are distinct. No measured ATMOS results are asserted.
[D1] Source deck — SanDisk ATMOS Enterprise Offerings Executive Proposal, 1 Oct 2026
User-provided source. Original slides 3–7, 10–14 supply offering names, execution boundaries, OEM study, pilot assumptions and economic allowances. Revision retains A/B/C; whole-layer pipeline is removed at the user’s request. New diagrams and worked examples are proposed analysis.
[S1] Lloyds Banking Group — AI-driven benefits, 29 Jan 2026
https://www.lloydsbankinggroup.com/media/press-releases/2026/lloyds-banking-group/ai-driven-benefits-2026.html
Athena used by 20,000 colleagues; reported average search-time reduction 66%. Not an ATMOS customer, disclosed GPU deployment, token trace or inference-cost comparison.
[S2] Qwen3-235B-A22B — model configuration
https://huggingface.co/Qwen/Qwen3-235B-A22B/blob/main/config.json
94 layers, 4 KV heads, head dimension 128, 128 experts, top-8. KV calculations assume BF16 values and full logical cached context; exclude duplication, block rounding and workspace.
[S3] Qwen3-30B-A3B — model configuration
https://huggingface.co/Qwen/Qwen3-30B-A3B/blob/main/config.json
48 layers, 4 KV heads, head dimension 128; 128 experts and top-8. Source deck/publisher model card: about 30.5B total and 3.3B active parameters.
[S4] AMD — EPYC 9355P specification
https://www.amd.com/en/products/processors/server/epyc/9005-series/amd-epyc-9355p.html
Public CPU reference: 32 cores, one socket, 128 PCIe Gen5 lanes and 12 DDR5 channels. All appliance population, cooling and network selections are proposed OEM study inputs, not certification.
[S5] Tenstorrent — vLLM platform plugin
https://github.com/tenstorrent/vllm-tt-plugin
Public precedent for a native platform plugin with loading, worker execution and scheduling. Does not certify ATMOS silicon, HBF/LPDDR access, full-model support or service rates.
[S6] NVIDIA Dynamo — disaggregated serving
https://docs.nvidia.com/dynamo/components/router/disaggregated-serving
Separate prefill/decode worker pools and KV handoff are documented. A cross-GPU/ATMOS deployment, its backend and cache interoperability must be implemented and qualified separately.
[S7] vLLM — disaggregated prefilling
https://docs.vllm.ai/en/latest/features/disagg_prefill/
Connector-based KV handoff; an ordinary chat API does not expose native cache state. Public framework capability does not imply an ATMOS decoder exists.
[S8] LMCache — KV management layer
https://docs.lmcache.ai/
Public KV-management and transfer framework. It is not an attention kernel, full ATMOS model runtime or proof of a compatible device layout.
[S9] Leviathan et al. — Fast Inference from Transformers via Speculative Decoding
https://proceedings.mlr.press/v202/leviathan23a.html
ICML 2023 algorithmic precedent for draft proposals and target acceptance/correction. Distribution preservation requires the correct algorithm, not voting or a quality classifier. No ATMOS timing or acceptance rate is supplied.
[S10] Kubernetes — device plugins
https://kubernetes.io/docs/concepts/extend-kubernetes/compute-storage-net/device-plugins/
Resource discovery/advertisement and allocation. Labels do not allocate NPUs or establish model readiness. Proposed Sandisk whole-device allocation and lifecycle are new product work.
[S11] DeepSeek-V3 — model configuration
https://huggingface.co/deepseek-ai/DeepSeek-V3/blob/main/config.json
Source deck retains publisher model geometry: approximately 671B total, 37B active, 256 routed plus shared expert, 58 MoE and 3 dense layers. MLA cache must be sized separately; Qwen GQA formula does not apply.
[I1] Internal ATMOS planning envelope
Source deck slides 5–6 and 12; supplied ATMOS proposal. Up to 128 GB HBF per E3.S, 100 GB application study budget, 8–16 GB LPDDR, 200 GB/s local-read target. Unqualified device targets: not production specification, native runtime support, price or throughput.